## Slide 1: Fifth Meeting of THE COMMUNICATIONS SECURITY, RELIABILITY, AND INTEROPERABILITY COUNCIL VIII
September 21, 2022

## Slide 2: Open Meeting & Welcome Suzon Cameron, DFO

## Slide 3: Opening Remarks
CSRIC VIII Co-chair
Nasrin Rezai, Verizon

## Slide 4: Presentation
WG1: Co-chairs
Brian Daly, AT&T
Travis Russell, Oracle
Report on Vulnerabilities in HTTP/2

## Slide 5: Working Group 1: 5G Signaling Protocols Security
September 21, 2022
Co-chairs:
Brian Daly, AT&T
Travis Russell, Oracle Communications
FCC Liaison: Ahmed Lahjouji

## Slide 6: Working Group 1: Background
The Chairwoman of the FCC directs CSRIC VIII to examine and address security vulnerabilities associated with the newly adopted 5G signaling protocol, Hypertext Transfer Protocol Version 2 (HTTP/2), which, like the SS7 and Diameter signaling protocols considered in earlier CSRICs, is vulnerable to attacks. Researchers have discovered security issues related to the HTTP/2 protocol which could place millions of websites at risk of attack. CSRIC VIII will confirm these vulnerabilities and identify others, assess their potential for harm, and recommend safeguards to harden 5G networks and protect critical business and consumer data from these and other cyber threats. CSRIC VIII will also provide recommendations on how to remediate the risks associated with HTTP/2 and prevent them from carrying over to HTTP/3, the next release of the protocol.

## Slide 7: Working Group 1: Objectives
The FCC has learned of four main vulnerabilities and attack vectors related to HTTP/2:
  (1) slow read attacks, which call on a malicious client to read responses very slowly;
  (2) HPACK Bombs, which are malicious archive files designed to crash the program or system reading them and often disable antivirus software;
  (3) Dependency Cycle attacks, which exploit a new flow mechanism designed to optimize networks to instead create an infinite loop which cannot be escaped; and
  (4) Stream Multiplexing Abuse, which uses security flaws in stream multiplexing functionality to crash servers, resulting in a denial of service to legitimate users.
We will research these as well as other vulnerabilities and attack vectors identified by industry through industry SMEs and WG member expertise.

## Slide 8
Working Group 1: Members
  *Also a CSRIC VIII Member
  Michael Bergman,* Consumer Technology Association
  Matt Carothers, Cox Communications
  Martin Goldberg,* National Security Agency
  Angel V. Gomez, Verizon Communications
  Stephen Hayes,* Ericsson
  Jithin Jagannath, ANDRO Computational Solutions
  Antwane Johnson,* FEMA
  Xiaoyang Lee, CISA
  John Marinho, CTIA
  Martin McGrath, Nokia
  Maureen C. Mclaughlin,* Satellite Industry Association
  Danny McPherson,* Verisign, Inc.
  Derek Peterson,* Wireless Broadband Alliance
  Mitch Rappard, Palo Alto Networks
  Mike Recchione, ATIS
  Greg Schumacher, T-Mobile
  Christopher Wendt, Somos, Inc.
Co-chairs: Brian Daly,* AT&T
Travis Russell,* Oracle
FCC Liaison: Ahmed Lahjouji

## Slide 9
Working Group 1: Alternates*
* Alternates are not a member of the Working Group and may not vote.
  Adam Barron, Verizon Communications
  Martin C. Dolly, AT&T, Inc.
  Carroll Gray-Preston, ATIS
  J. David Grossman, CTA
  Brandon Hinton, Satellite Industry Association
  Bradley Jackson, Verizon Communication
  Navin Jaffer, CISA
  Yong Kim, Verisign, Inc.
  Mark Lucero, FEMA
  John Mattson, Ericsson

## Slide 10: Working Group 1: Deliverables/Schedule
WG virtual meetings (biweekly) continue
  Research/examine security vulnerabilities and attack vectors
#1 - Report on Security Vulnerabilities in HTTP/2, September 2022
  Presenting today for the Council’s consideration and vote
#2 - Report on Best Practices to Mitigate Vulnerabilities in HTTP/2 and HTTP/3, June 2023

## Slide 11: Report #1 - Executive Summary
5G is a departure from traditional wireless networks
  It is not the next evolution building on 4G
  5G is a completely new architecture with “new” technology
  5G is built using IT and cloud technology
The signaling protocol used within the 5G core network and other parts of 5G (such as OSS/BSS) is HTTP
  The network core uses HTTP/2 while some support systems may use HTTP/1
  This raises concerns around known vulnerabilities in the HTTP protocol

## Slide 12: Report #1 - Executive Summary
The FCC tasked WG1 to identify any vulnerabilities 5G signaling vulnerabilities associated with the HTTP/2 protocol specifically
The first deliverable is this report identifying those vulnerabilities
The second deliverable is a report on how to mitigate those vulnerabilities and provide recommendations for both industry and the FCC

## Slide 13: Methodology
While there are many vulnerabilities in HTTP/2 for networks with public access (the Internet) these same vulnerabilities do not necessarily pose a threat in a closed network such as 5G
  This was taken into consideration as we examined all known vulnerabilities and explored other potential threats
  This report then identifies the vulnerabilities that pose a threat to 5G core networks rather than all vulnerabilities of HTTP
  The WG looked at existing industry sources, input from the FCC, as well as presentations from subject matter experts
  This report does not discuss mitigations, as that will be the topic of the next report due June 2023

## Slide 14: References and Sources
INDUSTRY SPECIFICATIONS
3GPP 28.533 Management and orchestration; Architecture framework
3GPP TR 29.893 Study on IETF QUIC Transport for 5GC Service Based Interfaces
3GPP TS 33.117 v17.0.0; Catalogue of general security assurance requirements
IETF RFC 7540; Hypertext Transfer Protocol Version 2 (HTTP/2); May 2015
INDUSTRY WHITE PAPERS
The 3GPP defined Service Based Management Architecture White Paper (Nokia Bell Labs)
QUIC and HTTP/3; Ericsson presentation, April 2020
RESEARCHER CLAIMS
HTTP/2: In-depth analysis of the top four flaws of the next generation web protocol; Imperva, Hacker Intelligence Initiative; August 2016, V1
Signalling Security Analysis: Is HTTP/2 Secure in 5G Core Network?; Hu, Xinxin; Liu, Caixia; You, Wei; Zhao, Yu; National Digital Switching System Engineering & Technological Research Center; Zhengzhou China
HTTP/2: The Sequel is Always Worse; Kettle James
5G Network Slicing Security; McDaid, Cathal, AdaptiveMobile; Feb 2022
We are very grateful to all the SMEs that presented to WG1. Your inputs were very valuable to our work.

## Slide 15: Use of HTTP/2 in 3GPP Systems
HTTP/2 has never before been used in 3GPP Standards-based systems
  Industry relied on proprietary signaling technology signaling system #7 (SS7) and Diameter (4G signaling)
  The 3GPP has specified that HTTP/2 (or later versions) be the signaling protocol of choice for 3GPP systems
  The 3GPP has specified HTTP/2 for use in the Service Based Architecture (SBA) and the SBA Management Architecture (SBMA)
  The GSMA has also specified HTTP/2 be used between networks to support roaming
    The GSMA is also specifying the use of HTTP/2 in other parts of the network
    eSIM management interfaces use HTTP/2
  The ORAN also uses HTTP/2 for orchestration and management interfaces

## Slide 16: What is an SBA?
In previous generations of wireless, the 3GPP system used point-to-point interfaces between network functions
  The network has become more dynamic with virtualization & more functions
  This has made such an architecture unmanageable
  The 3GPP defined the SBA in 3GPP TS 23.501
  The SBA does not require the use of every network function for every mobile session – a departure from previous generations of wireless
  This illustration also demonstrates the increase in network functions used by the network core within the SBA (next slide)
  The Service Communication Proxy (SCP) is not shown in this illustration but also serves a key role in the SBA architecture

## Slide 17: What is an SBA?
The protocol specified for use between each network function is HTTP/2
HTTP/2 is the lowest version of HTTP allowed to be used in the SBA

## Slide 18: What is SBMA?
Prior to 5G, the management system consisted of two functions
  An element manager
  A network manager
  A “reference point” was then identified between the two functions (ltf-N)
  Management interfaces were then defined for ltf-N
Starting with 5G, the architecture was changed to align with a service-based architecture

## Slide 19: What is the SBMA?
The SBMA is comprised of mgmt services
  Configuration
  Performance
  Fault mgmt.
  New services are being added in subsequent releases of the specs
Each 5G network function type has its own set of services
  This provides flexibility and allows suppliers to provide their own set of services for their NFs

## Slide 20: Standardization of HTTP
The IETF defines the specifications for the Hyper Text Transfer Protocol (HTTP)
  The protocol was developed for internet users to access and retrieve website information
  There have been 4 iterations of HTTP since its inception in 1991
  HTTP/2 was released in 2015 as a major revision & replacement to HTTP/1.1
  It provided better efficiency and reduced online latency
HTTP/2 is defined in IETF RFC 7540

## Slide 21: Standardization of HTTP
HTTP/3 is still a work in progress
  HTTP/2 runs on TCP, which introduces latency issues within signaling
  Google has defined an adaptation layer called Quick UDP Internet Connections (QUIC) that emulates the connection-oriented features of TCP over a UDP connection
  UDP is much faster than TCP but uses “best-effort” to delivery (connection-less) but QUIC will resolve this issue
HTTP/3 and QUIC has not yet been endorsed by the 3GPP for use in 3GPP networks
  There is still work to be done in the IETF
  The 3GPP continuously profiles the work of IETF and updates 3GPP specifications accordingly

## Slide 22: Analysis of HTTP Vulnerabilities
HTTP/2 supports a wide range of applications including the WWW, Internet, and specialized services (such as micro-services)
The SBA/SBMA is one example of a specialized service
While it is possible to use these known vulnerabilities researched by this CSRIC against any Internet connected entity, the 5G SBA/SBMA is not connected to the Internet, and is a closed network
  To gain access to the SBA/SBMA would require compromise of the network from within a company’s resources
  This may be possible but is highly unlikely
  This WG1 will provide recommendations to prevent insider threats in its next report

## Slide 23: Analysis of HTTP Vulnerabilities
The 1st assumption of WG1 is that the 5G core has deployed robust network perimeter defenses (between closed networks) around the SBA/SBMA functions
The 2nd assumption is that these vulnerabilities would be second or subsequent stages in a multi-stage attack
  An earlier stage would be to compromise access to the SBA/SBMA
  This means that some of the vulnerabilities that we researched would not be applicable to a 5G network core, or have minimal impact

## Slide 24: Client initiated attacks on servers
This type of attack is initiated against HTTP/2 clients HTTP/2 servers
  Slow Read Attack
  HPACK Bombs
  Dependency Cycle Attacks
  Stream Multiplexing Attacks
  URL Prefix Injection
  SBA customer attack

## Slide 25: Slow Read Attack
This vulnerability was identified by the FCC as an example of vulnerabilities and included in the WG1 tasking
  Attacker sends valid HTTP requests to the server
  Attacker reads responses very slowly
  This keeps the connection alive without timing out
  This results in the server dedicating resources to the connection
  Eventually resources are overwhelmed or resources flooded with such requests blocking other requests from getting through
  This attack is not explicitly banned by RFC 7540

## Slide 26: HPACK Bombs
This vulnerability was identified by the FCC as an example of vulnerabilities and included in the WG1 tasking
  RFC 7540 permits the sender to define the max size of the header compression table
  The RFC does not restrict the size of individual headers
  The attacker inserts a header field that is exactly the size of the HPACK dynamic header table in the dynamic header table
  The attacker than sends requests to expand the header field in the dynamic table repeatedly
  The attacks can quickly result in gigabyte-level storage rqmts on target machine
  The end-result is a DoS as the target servers resources are exhausted

## Slide 27: Dependency Cycle Attacks
This vulnerability was identified by the FCC as an example of vulnerabilities and included in the WG1 tasking
  RFC 7540 allows a stream to give an explicit dependency on another stream
  This allows the server to prioritize stream handling
  The dependency graph must be a strict tree – processing a loop or cycle in the graph can cause unpredictable behavior (infinite loops, i.e.)
  The result is a DoS as the target servers resources are exhausted

## Slide 28: Stream Multiplexing Attacks
This vulnerability was identified by the FCC as an example of vulnerabilities and included in the WG1 tasking
  An HTTP/2 stream represents a single request/response cycle
  Once the cycle is closed, RFC 7540 requires the stream identifier is not used again over the same connection
  If an implementation of the HTTP/2 protocol stack on a server fails to follow this requirement, the result is a DoS
The WG1 classified this as an implementation vulnerability, defined in section 6.1.7

## Slide 29: URL Prefix Injection
The value of the scheme header is meant to be HTTP or HTTPS but it supports arbitrary bytes
  Some protocol stacks (implementations) use it to construct a URL w/out performing validation
  This allows the attacker to override the path and possibly poison the cache or create a server side request forgery (SSRF) vulnerability
  While the RFC allows this, implementations lacking validation this vulnerability can be affective
  Since the specific 5G implementations are unknown this was considered as a protocol level vulnerability
  While this may not be an implementation vulnerability, it was included in the report for more thorough review and classification for the next report

## Slide 30: SBA customer attack
The following sequence illustrates this attack
  Attacker compromises or takes control over a Session Mgmt Function (SMF) (consumer) and is now ”inside” the SBA
  The compromised SMF mounts an SBA DoS attack against the Universal Data Mgmt (UDM) (producer) using the slow read vulnerability
  The 5G network operations degrade under this attack by the compromised SMF instance
This attack requires earlier steps to compromise the SMF (insider attack)

## Slide 31: Heist Attack
This attack is based on vulnerabilities in other protocols and implementation shortfalls
“…because SSL/TLS does not hide the length of the clear-text message (a weakness that has been well-known to the security community since 1996) adversaries can directly infer the length of the response before encryption.”
With this information, the attacker can utilize the details of other protocols and web-browser activity including the handling of 3rd party cookies to extract encrypted behavior
More information and its applicability (as well as mitigation) on this type of attack will be provided in the final report

## Slide 32: Implementation Vulnerabilities
Implementation vulnerabilities are considered as “bugs” in specific products
  The poor implementation of the protocol stack can result in vulnerabilities being exploited
  Each product deals with this in their own way, and report on these bugs through patch reports
  This may be caused by failure to
    Follow protocol specifications correctly
    Observe good cybersecurity practices such as input data validation
    Errors in coding
These vulnerabilities were not considered by WG1, as they are tracked through CVEs and fixed by each individual product supplier through patches – it is outside the scope of WG1

## Slide 33: Conclusions
The scope of this report is the analysis of vulnerabilities relative to HTTP/2 in the 5G context
The second report will provide mitigations and recommendations for industry and the FCC
While the use of HTTP/1.1 may be allowed in some parts of the 5G ecosystem, the known vulnerabilities suggest the use of HTTP/2 or later should be standardized for all 5G signaling

## Slide 34: Discussion
WG1: Co-chairs
Brian Daly, AT&T,
Travis Russell, Oracle
Report on Vulnerabilities in HTTP/2

## Slide 35: Call For Vote
Report on Vulnerabilities in HTTP/2
CSRIC VIII Co-chair
Nasrin Rezai, Verizon

## Slide 36: Presentation
Report on Recommended Best Practices to Improve Comm. Supply Chain Security
WG5: Co-Chairs
Todd Gibson, T-Mobile
Padma Sudarsan, VMware

## Slide 37: Working Group 5: Managing Software & Cloud Services Supply Chain Security for Communications Infrastructure
September 21, 2022
Co-Chairs: Todd Gibson, T-Mobile & Padma Sudarsan, VMware
FCC Liaison: Saswat Misra

## Slide 38: Working Group 5: Background
The Chairwoman of the FCC directs CSRIC VIII to review risks to service provider operations from attacks in service providers’ software and cloud services stacks and develop mitigation strategies for these vulnerabilities. In order to improve supply chain security in the communications industry, the FCC has barred the use of Universal Service Fund support to pay for equipment and services produced or provided by any company posing a national security threat to the integrity of communications networks or the communications supply chain, and the FCC will be reimbursing providers to remove, replace, and dispose of insecure equipment and services. Additionally, prior CSRIC work, such as the CSRIC IV Report on Cybersecurity Risk Management and Best Practices (March 2015), and the CSRIC II Report on Cybersecurity Best Practices (March 2011), focused on attacks that mostly affect traffic on the network or attacks on users through the network.
However, recent breaches of trusted vendors of software have exposed risks in other segments of the supply chain that have resulted in previously trusted systems becoming compromised. Specifically, attackers have inserted malware in to signed code with valid, but compromised, digital certificates. These recent breaches have highlighted that the threat is pervasive and extends well beyond the telecommunications network itself to software components and cloud-based services that service providers rely on to manage and operate their networks. Attacks on these operational networks could have a significant impact on emergency 911 calls and national security communications.
The FCC further directs CSRIC VIII to recommend best practices to mitigate the risks for each vulnerability it identifies, considering the matrix of capabilities of large and small service providers, large and small software vendors, and large and small cloud service providers.

## Slide 39
  *Also a CSRIC VIII Member
Rob Alderfer,* Charter Communications
Tom Anderson, ATIS
Colin Andrews, Telecommunications Industry Association
Jan H.L. (John-Luc) Bakker, BlackBerry Corporation
Donna Bethea-Murphy,* Inmarsat
Shirley Bloomfield,* NTCA-The Rural Broadband Association
Matt Carothers, Cox Communications
Josh Cech, S&T Telephone Cooperative Association
Dana Golub,* Public Broadcasting Service
Anu Jagannath, ANDRO Computational Solutions
Mohammad Khaled, Ericsson
Jason Lish,* Lumen Technologies, Inc.
Timothy May,* NTIA
Martin McGrath, Nokia
Maureen C. Mclaughlin,* Satellite Industry Association
George Popovich, Motorola Solutions
Travis Reutter,* ACA Connects- America's Communications Association
Nasrin Rezai,* Verizon Communications
John Roznovsky, Mavenir
Sean Scott,* SecuLore Solutions
Jim Stringer, AT&T, Inc.
Richard “Dick” Tenney, CISA
Claire Vishik,* Intel
Kelly Williams, NAB
Timothy Wilson-Johnston, Cisco Systems, Inc.
Henry Young,* BSA | The Software Alliance
Co-Chairs: Todd Gibson, T-Mobile & Padma Sudarsan,* VMware
FCC Liaison: Saswat Misra
Working Group 5: Members

## Slide 40
* Alternates are not a member of the Working Group and may not vote.
  Reza Arefi, Intel
  Tom Breen, SecuLore Solutions
  Mark Carmel, CISA
  Cathleen M. Dwyer, Verizon Communications
  Brandon Hinton, Satellite Industry Association
  Brian Hurley, ACA Connects
  Tamber Ray, NTCA - The Rural Broadband Association
  Mark Roy, Public Broadcasting Service
  John A. Schiel, Lumen Technologies, Inc.
  Mike Regan, Telecommunications Industry Association
  Jason VonBargen, Charter Communications
  Timothy Youngblood,** T-Mobile
Working Group 5: Alternates*
  ** Also, a CSRIC VIII Member

## Slide 41
Report #1 - Best Practices to Improve Communications Supply Chain Security
  Primary focus is on the Software Supply Chain for the first report.
  Due Date: September 2022
  Submitting today for full Council consideration
Report #2 - Best Practices to Improve Supply Chain Security of Infrastructure and Network Management Systems
  Focus will be on Hardware Supply Chain and Implicit Trust of NMS Software Supply Chain
  Due Date: June 2023
Working Group 5: Report Schedules

## Slide 42
Normative Sections
  Executive Summary, Introduction, Objective, Scope, and Methodology
Recent Software Supply Chain Attacks & Vulnerabilities
  What recent breaches of trusted supply chain software vendors had the most impacts?
  What was the taxonomy of the attack and what could have been done to prevent and/or mitigate?
Analysis of Current Industry and Governmental Efforts
  Collectively, what is the industry and various federal agencies doing to improving supply chain security?
Description, Findings, and Recommendations
  Work Group’s description of a Secure Software Supply Chain
  Summary of Key Findings and Recommendations
Report #1 Structure

## Slide 43
SolarWinds
  Their build server was compromised by a state-sponsored threat actor that embedded backdoor code into a legitimate SolarWinds library.
  This backdoor enabled access into the victim’s environment which they used to load malicious software in both memory and storage resulting in compromised platforms.
Apache Log4j Flaw
  This was a vulnerable open source software that was released into the marketplace.
  Log4j is sourced from public repositories and embedded into trusted commercial software.
  The flaw allows an attacker to orchestrate a remote code execution attack through LDAP, for example, which stores user identification, passwords, and computer accounts.
Kaseya VSA
  An authentication bypass vulnerability allowed attackers to compromise the VSA software and distribute a malicious payload through hosts managed by the VSA software.
  The malicious payload would then execute a ransomware attack via SQL injection on identified client databases.
Recent Software Supply Chain Attacks

## Slide 44
Federal Agencies
  Executive Order 14028
  NTIA Minimum Elements for a Software Bill of Materials (SBOM)
  NIST’s Guidance on Practices that Enhance Software Supply Chain Security
  Dept. of Commerce and DHS – Assessment of the Critical Supply Chain supporting U.S. Information and Communications Technology (ICT)
  NSTAC’s Report to the President on Software Assurance
  CISA’s Vulnerability Exploitability eXchange (VEX)
Industry Standard’s Bodies and Forums
  GSMA’s Network Equipment Security Assurance Scheme
  ATIS’ 5G Network Assured Supply Chain standard
  5G Americas’ Security for 5G white paper
  BSA’s Framework for Secure Software
  TIA’s SCS 9001™ Supply Chain Security Management System
  Synopsys’ 2022 Open Source Security and Risk Analysis Report
  Supply Chain Levels for Software Artifacts (SLSA - aka salsa)
Current Industry/Governmental Efforts

## Slide 45
Secure Software Supply Chain
Secure Software Supply Chain is a set of practices that enable organizations to adjust the way they securely consume proprietary or open source packages – both first- and third-party – from source code to operationalization at a sustained high speed and quality relative to their accepted risk level.

## Slide 46
Change in Paradigm impacting Current Software Supply Chain As service providers transform and evolve into the next generation of service offerings, new vulnerabilities are emerging, and the attack surfaces are growing – including but not limited to:
  Virtualization of Software Resulting in Vertical and Horizontal Disaggregation
  Wide adoption of Open Source Software
Modernization of the Supply Chain Even with the published supply chain enhancements discussed in this report, there are still gaps in the industry today that need modernizing, including but not limited to:
  Software Bill of Materials (SBOM) Enhancement Considerations
    Machine Readable, HW/SW Components/Subcomponents, Embedded Free and Open Source Software (FOSS), Data Access, End-of-Life/Support, Provenance, Cryptographic Protections, and more.
  Other Supply Chain Risk Management (SCRM) Enhancement Considerations
    Cryptographic Agility, Public Communications related to SCRM Attacks/Events, and Cloud Providers and/or Software Vendors with Established CI/CD Pipeline.
Summary of Key Findings

## Slide 47
Lack of a Complete and Definitive Standard in Software Supply Chain
  These emerging public and private artifacts of guidance, specifications, and/or standards have notable differences and conflicts that creates confusion in the industry – one example below:
Summary of Key Findings

## Slide 48
Lack of a Complete and Definitive Standard in Software Supply Chain (continued)
  To advance the industry forward towards developing a sustainable and repeatable process for software supply chain security, the industry needs to collaborate to evaluate the feasibility of recommendations including:
    Foundational Processes – SBOM Minimum Data Fields, Software Identification Tags, and SBOM Automation
    Risk Management Processes – Software Provenance Authority, Software Author/Supplier Identity, and Author/Supplier Reputation
    Vulnerability Management Processes – Software Chain of Custody, Vulnerability and Exposure Disclosures, Unpatched Vulnerabilities, and Software Immutability.
Summary of Key Findings

## Slide 49
Cybersecurity Operations – Runtime Security
  Runtime Application Self-Protection (RASP) is an emerging security capability that enhances the security monitoring on the operating platforms and applications.
  Additionally, Cloud Workload Protection Platform (CWPP) is another runtime security solution that is applicable to cloud-based services.
  Referencing the recent software supply chain cyber attacks, runtime security could have been a security capability that may have alerted the service provider, software vendor, and/or cloud service provider to the attack(s).
Common Best Practices for Software Supply Chain
  Some common software best practices are listed below. While they are not directly impacting software supply chain, they are contributing towards secure delivery of software.
    Developer Training
    Software Composition Analysis
    Security Scanning
    Outsourced Software Development
    Credential Management
Summary of Key Findings

## Slide 50
General Guidance for Organizations regarding SBOMs
  Expected SBOM Mandates for Federal Suppliers and SBOM Generation and Consumption
Common Software Supply Chain Security Recommendations
  Grouped into 5 Groupings:
    Secure Development
    Free and Open Source Software (FOSS)
    Cyber and Supply Chain Risk Management and Processes
    Cybersecurity Operations
    Standardization Opportunities
  Recommended Best Practice Tiers (1 through 3 with 1 being Most Critical)
  19 Vulnerabilities Identified & 59 Recommendations Provided
Summary of Recommendations

## Slide 51
The Commission can assist providers of all sizes with software and cloud services supply chain security by offering resources to increase providers’ awareness of software and cloud services supply chain risks and describing methods of enhancing software supply chain security.
The Commission could engage with CISA and NIST to support an effort to create universal standards and specifications for software supply chain security.
The Commission could engage with CISA and NIST to support the standardization of the SBOM formats, uses, and deployments since these are critical to addressing the software supply chain security vulnerabilities globally.
This work group recommends to the Commission that a broader study on open source software security be done in order to objectively understand the potential risks that open source software poses.
Other Recommendations for the Commission

## Slide 52: Questions?
Work Group 5’s Report #1 Best Practices to Improve Communications Supply Chain Security
  Primary focus is on the Software Supply Chain for the first report.
  Due Date: September 2022
  Submitting today for full Council consideration
Co-Chairs: Todd Gibson, T-Mobile & Padma Sudarsan, VMware

## Slide 53: Discussion
Report on Recommended Best Practices to Improve Comm. Supply Chain Security
WG5: Co-Chairs
Todd Gibson, T-Mobile
Padma Sudarsan, VMware

## Slide 54: Call For Vote
Report on Recommended Best Practices to Improve Comm. Supply Chain Security
CSRIC VIII Co-chair
Nasrin Rezai, Verizon

## Slide 55: Presentation
WG2: Co-chairs
Mike Barnes, Mavenir
George Woodward, RWA
WG2: Promoting Security, Reliability, and Interoperability of ORAN Equipment

## Slide 56: Working Group 2: Promoting Security, Reliability, and Interoperability of Open Radio Access Network Equipment
Sept 21, 2022
Co-chairs:
Mike Barnes, Mavenir
George Woodward, RWA
FCC Liaison: Zenji Nakazawa

## Slide 57: Working Group 2: Background
The Chairwoman of the FCC directs CSRIC VIII to provide recommendations to advance security, reliability, and interoperability of Open Radio Access Network (ORAN) equipment in the United States and what new efforts can be undertaken to support secure and interoperable ORAN design and deployment.
The Radio Access Network (RAN) is the final link between the network and the phone. It includes the antennae on towers, buildings, and in stadiums, plus the base stations. When a consumer makes a call or connects to a remote server, the antenna transmits and receives signals to and from the consumer’s mobile phone or other handheld device. The signal is then digitalized in the RAN base station and connected into the network.
The introduction of ORAN enables mobile network operators to use equipment from multiple vendors and still ensure interoperability.

## Slide 58: Working Group 2: Objectives
CSRIC has previously considered security risks in emerging 5G networks.
CSRIC VIII will build on this work and expand it as one part of its exploration of the development and deployment challenges facing ORAN technology, including the extent ORAN technology may increase the threat attack surface and how best to mitigate such security challenges.
Further, CSRIC VIII will consider how the FCC can support the goals of developing and deploying secure, open and interoperable networks when the FCC participates in standards-setting bodies like 3GPP and the Alliance for Telecommunications Industry Solutions.

## Slide 59
Working Group 2: Members
  *Also a CSRIC VIII Member
Rob Alderfer,* Charter Communications
Robert Dew, CISA
Marla Dowell,* NIST
Andrew L. Drozd,* ANDRO Computational Solutions
Russ Gyurek, Cisco Systems, Inc.
Javed Khan,* Altiostar Networks
Michael Loushine, AT&T, Inc.
Jennifer Manner,* Hughes Communications
Martin McGrath, Nokia
Jack Nasielski, Qualcomm Technologies, Inc.
Scott Poretsky, Ericsson
Vishwanath Ramamurthi, Verizon Communications
Stefan Saroiu, Microsoft Corporation
Tom Sawanobori,* CTIA
Tim Schram,* NARUC
Nick Solano, Qcommunications, LLC
Eric Tamarkin, Samsung Electronics America
Jean Trakinat, T-Mobile
Claire Vishik,* Intel
Henry Young,* BSA | The Software Alliance
Tim May,* NTIA
FCC Liaison: Zenji Nakazawa
Co-chairs: Mike Barnes,* Mavenir
George Woodward,* RWA

## Slide 60
Working Group 2: Alternates*
* Alternates are not a member of the Working Group and may not vote.
  Reza Arefi, Intel
  Afeite Dadja, CTIA
  Brian Daly, AT&T
  Arvind Kumar, Mavenir
  Heidi Obermeyer, BSA | The Software Alliance
  Anand Palanigounder, Qualcomm
  Sanil Rama Chandran, Samsung
  James B. Ramsay, NARUC
  Nancy Shemwell, Rural Wireless Association
  Lakhbir Singh, Charter Communications
  Matthew Sneed, Hughes Communications
  Ryan Stokes, Rural Wireless Association
  Lap Tse, Verizon Communications
  Timothy O. Woods, ANDRO Computational Solutions

## Slide 61: Working Group 2: Deliverables/Schedule
14-June 2022 - First Draft complete
13-Sept-2022 – Begin Final Review
15-Nov-2022 - Paper and Slides complete, submitted FCC
December 2022: Report on Challenges to the Development of ORAN Technology and Recommendations on How to Overcome Them

## Slide 62: Next Working Group 2 Meeting Agenda
Continue Final Review
20-21 Sept 2022 - Face to Face/Virtual Meeting (Boulder, CO)

## Slide 63: Discussion
WG2: Co-chairs
Mike Barnes, Mavenir
George Woodward, RWA
WG2: Promoting Security, Reliability, and Interoperability of ORAN Equipment

## Slide 64: Presentation
WG3: Co-chairs
Micaela Giuhat, Microsoft
John Roese, Dell
WG3: Leveraging Virtualization Technology to Promote Secure, Reliable 5G Networks

## Slide 65: Working Group 3: Leveraging Virtualization Technology to Promote Secure, Reliable 5G Networks
Co-chairs:
Micaela Giuhat, Microsoft
John Roese, Dell
FCC Liaison: Jeff Goldthorp

## Slide 66: Working Group 3: Background
CSRIC VIII will develop recommendations for how vendor-agnostic, horizontal stack solutions for 5G can be promoted to foster a diverse, competitive, and more secure 5G environment despite the wider attack surface presented. These recommendations should address ways to provide opportunities for smaller vendors that cannot yet manufacture all parts of a vertically integrated, traditional 5G stack.
In its first report on this subject, CSRIC VIII’s will include recommendations on ways in which funds can be made available to promote virtualized environments that result in improved 5G security and reliability; recommendations on ways to promote and overcome obstacles to the availability of virtualized central units (vCU) and virtualized distributed units (vDU) to increase 5G vendor diversity; best practices for reliability and interoperability that should be used by small businesses that contract or outsource as part of a multi-vendor 5G implementation; and other ways to promote a diverse 5G environment to improve 5G security and reliability. CSRIC VIII will also identify whether any additional work is needed from standards bodies such as 3GPP and ETSI on virtualization issues, such as addressing security risks relating to application programming interface (API) security.
Scope should include virtualization of the system which would include the core plus the CU, DO and possibly RU.
Virtualization in this context is more about the horizontal layering abstractions than the creation of open interfaces within a layer (E.g. eCPRI etc) However we should discuss if we have an opinion on “in layer open interfaces” being in scope.

## Slide 67: Working Group 3: Objectives
Review lessons learned from use of virtualization and higher vendor diversity in strengthening security, increasing competition, and creating a more secure supply chain
Gather input from researchers, technologists and thought-leaders and standard organizations on availability of solutions, and technical issues to be addressed
Perform an assessment of implementation best practices
  Perform comparison between virtualized and non-virtualized security vulnerabilities (theoretical and maybe practical?) in a 5G network
  Review results from test labs or real-life deployments around the world
  Identify issues to be addressed (e.g., API security)
Advise & recommend accordingly on how best to support a secure diverse vendor ecosystem:
  Funding
  Standards
  Integration best practices
  Ecosystem structures (who plays what roles in the open virtualized 5G ecosystem)
Report on How Virtualization Technologies can be Used to Promote 5G Security and Reliability
Report on Recommendations on the Role of the FCC in Promoting the Availability of Standards for More Secure, Reliable 5G Environment Through the Use of Virtualization Technology

## Slide 68
Marla Dowell,* NIST
Andrew L. Drozd,* ANDRO Computational Solutions
Bob Everson, Cisco Systems, Inc.
Michael Gallagher, Verizon Communications
Martin Goldberg,* National Security Agency
Javed Khan,* Altiostar Networks
Douglas Knisely, Qualcomm Technologies, Inc.
Jennifer Manner,* Hughes Communications
Serge Manning, T-Mobile
Timothy May, NTIA
Martin McGrath, Nokia
William Mikucki,* Comtech Telecommunications Corp.
Keith O’Brien, Palo Alto Networks
Jitendra Patel, AT&T, Inc.
Leo Popokh, ATIS
Stere Preda, Ericsson
Tom Sawanobori,* CTIA
Jane Shen, Mavenir
Paul Steinberg,* Motorola Solutions
Frank Suraci, CISA
Peter Tomczak,* FirstNet Authority
Claire Vishik,* Intel
Damien Whaley, Cox Communications
George Woodward, Rural Wireless Association
Working Group 3: Members
  FCC Liaison: Jeff Goldthorp *Also a CSRIC VIII Member
Co-chairs: Micaela Giuhat,* Microsoft
John Roese,* Dell
New workgroup primary member

## Slide 69
  Reza Arefi, Intel
  Afeite Dadja, CTIA
  Kevin Green, FirstNet Authority
  Bryan Larish, Verizon Communications
  Doug Montgomery, NIST
  Vishwamitra Nandlall, Dell Technologies
  Scott Poretsky, Ericsson
  Rowland Shaw, Dell Technologies
  Matthew Sneed, Hughes Communications
  Megan Stapleton, Comtech Telecommunications Corp.
  Darrell Stogner, Motorola Solutions
  Ryan Stokes, Rural Wireless Association
  Richard Tenney, CISA
  Timothy Woods, ANDRO Computational Solutions
Working Group 3: Alternates*
* Alternates are not a member of the Working Group and may not vote.
New alternate member

## Slide 70: Working Group 3: Milestones
Report on How Virtualization Technologies can be Used to Promote 5G Security and Reliability - December 2022
Report on Recommendation on the Role of the FCC in Promoting the Availability of Standards for More Secure, Reliable 5G Environment Through the Use of Virtualization Technology - June 2023

## Slide 71: Working Group 3: Recap of Speaker Presentations
Date | Speaker | Entity | Topic
1/13 | Dr. Jithin Jagannath and Dr. Keyvan Ramezanpour | ANDROS Computational Solutions, LLC | Security Vulnerabilities in Coexistence of 5G and WiFI 6/6E
1/27 | Sundeep Rangan (Associate Director), Garg Siddharth, Elza Erkip, Christina Poepper | NYU Wireless | Introduction to NYU Wireless Center, Research direction pursing in 5G Security
2/10 | Dr. Ian Levy (NCSC Technical Director) | UK Cyber Security Center | UK for telecoms security
2/24 | Dr. Suku Nair (Ph.D, P.E., Director, SMU AT&T Center for Virtualization | SMU | 5G Security and Inter-Operability: Opportunities and Challenges
3/10 | Nagendra Bykampadi (Head of End-to-End Security Architecture, Assurance, and Ops); Co-chair O-RAN SFG | Rakuten Symphony | Security in a cloud native based Open vRAN
4/14 | John Morello | Palo Alto | NIST publication SP800-190 A container security guide. https://csrc.nist.gov/publications/detail/sp/800-190/final
4/28 | Scott Poretsky, MSEE, CISSP, Director of Security MANA Network Product Solutions | Ericsson | ZTA for Secure 5G Cloud Deployments
6/9 | Leo Popokh | HPE | 5G Slice Creation in compliance with 3GPP and ETSI

## Slide 72: Working Group 3: Deliverables/Schedule
Scope and Methodology Agreement December 7th, 2021
Create list of SMEs and other industry bodies to be invited January 2022
Finish gathering of information June 2022
Create paper outline/sections (2-day DC workshop) July 20-21, 2022
Assign individual contributors to draft paper sections Q3 2022
Draft paper complete End October
Collate, edit, finalize 1st paper December 2022
Start working on 2nd milestone End Q4 2022
Completed
Completed
Completed
Completed
Completed

## Slide 73: Working Group 3: Next Steps
Virtual workshop to complete draft report – September 21
Workshop Agenda:
  Document review
  Start recommendations

## Slide 74: Work Group 3 Expert Presentation Summaries

## Slide 75: Presentation 1: Security Vulnerabilities in Coexistence of 5G and WiFI 6/6E Presenter: Dr. Jithin Jagannath and Dr. Keyvan Ramezanpour from ANDROS Computational Solutions, LLC
Highlights:
Review of existing security vulnerabilities in the current 5G and Wi-Fi networks as a standalone network such as Layer 2 security.
Virtualized RAN and virtualized core:
  Most of the virtualization is currently happening on the core side.
  Virtualized core is most vulnerable due to their big data centers with highest risk of security compared to the virtualized RAN, given RAN represents the highest portion of the network and is expensive to be fully secure.
Virtualization and Access Network:
  If the virtualization technologies do not extend to the access network, it is to be contemplated as a potential risk exposing various gaps in-between.
  Similarly, access technologies that can reach the virtualized core exposes various security threats involved with virtualization.
Spectrum sharing with 5G, Wi-Fi, and attacker.
De-brief of various forms of authentications, Wifi Security Vulnerabilities (WPA3), and network architecture vulnerabilities.
Different types of attacks such as downgrade attack, side-channel attack, Dragonfly handshake protocol.
Counter measures: detection and provision.
5G coexistence new vulnerabilities within Wi-Fi, access network, and cellular core.
Wi-Fi off-loading:
  Instead of access through the towers, the access can also be via Wi-Fi. The hop from the Wi-Fi access vs the radio to the 5G core can expose potential vulnerabilities.
  Slicing extends to the radio network. Wi-Fi users from the non-3GPP devices if connect to the 5G core network is where the potential vulnerabilities can occur.

## Slide 76: Presentation 2: NYU Wireless Presenter: Sundeep Rangan (Associate Director), Garg Siddarth, Elza Erkip, Christina Poepper
Highlights:
Multivendor increases exposure
Untrusted segments of supply chain are Foundry and Digital hardware design, can lead to trojans in silicon and needs good focus, trusted segments being Network Equipment Provider and wireless carrier
Demonstrated user plane vulnerabilities for user data redirection & user impersonation due to missing integrity protection
Highlighted user data redirection, DNS request redirection and IP Header Checksum under the aLTEr attack
5G handover vulnerabilities for both intra and inter handover leading to either DoS or MitM relay
Recommended future work in:
  User plane Integrity Protection
  Enhanced Subscriber Privacy
  Interconnection Security
  Initial NAS Message Protection

## Slide 77: Presentation 3: UK for telecoms security Presenter: Ian Levy – technical director of national cybersecurity in NCSC (National Cyber Security Center) in UK
Highlights:
Brief history of 2017 cyberattacks in the UK telecom industry. The attack leading to 18 months long economic and technical modeling of telecommunications world with in-parallel understanding of how it actually works.
In total of 150 ways of attacks identified within telecom industry such as - espionage, using admin privileges, disrupt at small and large scale, national dependency, etc.
  TSR mentions in-depth management plane and signaling plane attacks.
  Brief discussion of TSR vs 5G tool-box.
Virtualization being adapted by the telecom industry for offering its robustness and resilience with added security benefits using modern signaling.
  Brief discussion on what does it mean to have virtualization vs containerization from the telecom and security aspect.
  VMs and containers mechanisms of virtualization and the difference between them with each technology’s pros and cons.
  Virtualization being a security function vs containerization is a scaling function.
  Containers are a mechanisms of virtualization. There are several other ways to virtualize than using containerization and VMs.
  With vibrant market of O-RAN virtualized industry, there are concerns with its alliance to security.
Strict policy compliance within security for telecommunications.
  Progression of technical specs into laws and having guidance.
  Vendor publishing statement of compliance as a strict regimen.
Hardware vs trusted software
  Dealing with hardware being easier than managing complex software from security perspective.
In order to gather more information regarding virtualized security, reach out to virtualization pioneers - VMware, Amazon, Google, Microsoft.
https://www.enisa.europa.eu/publications/5g-cybersecurity-standards/@@download/fullReport
https://www.enisa.europa.eu/publications/nfv-security-in-5g-challenges-and-best-practices/@@download/fullReport
Referenced documents in conversation

## Slide 78: Presentation 4: 5G Security and Inter-Operability: Opportunities and Challenges Presenter: Dr. Suku Nair (Ph.D, P.E., Director, SMU AT&T Center for Virtualizatio
Highlights:
5G security requires end-to-end security of all sections of the network, for example, RAN, Core, Internet, Control Plane, User Plane, Management Plane, etc.
Previously a mere authentication server used to suffice for the security, but with more complex systems such as 5G, server authentication is not enough. Therefore, introducing user authentication which also causing a lot more user attacks.
Issues with LTE/5G such as subscriber tracking, SS7 threats, no user plane integrity protection.
Various 5G security features based on CU/DU separation of gNB, subscriber privacy, unified authentication framework as well 5G for IOT, local network, authentication.
5G security comes with vertical (functional deployments) and horizontal (system including network, applications) levels.
Several outstanding challenges to manage the security for open-source platforms for cloud native, security automation, open source software, slice management, and IoT.
Example of a complex use case using a remote robotic surgery.
  Use of a fiber cable for its hepatic response in the beginning but extending the reach to wireless in the future with minimal latency, network delays between the surgeon and the robotic arm.
In conclusion:
3GPP does not standardize all aspects. Most of it is left to development and deployment.
Zero-trust architectures that defines each part of the network is independent making all aspects needs to be secure. This is a different approach to the older model of relying only on one trusted server.

## Slide 79: Presentation 5: Security in a cloud native based Open vRAN Presenter: Nagendra Bykampadi - Head of Security Architecture and Security Standards at Rakuten Symphony, and co-chair for the O-RAN Alliance Security Focus Group (SFG).
Highlights:
Overview comparison of RAN from a traditional layout to an open vRAN architecture.
Breakout of three types of open vRAN network topology into: aggregated DU vRAN, distributed DU vRAN, and distributed DU vRAN LLS-C1.
O-RAN's alliance to its architecture with its virtualized RAN network functions, hardware-software decoupling using cloud infra, and RIC.
  Note: Decoupling of software increases supply chain threats.
RAN specific landscape threats - additional functions (more code) reciprocates to additional attacks on the system.
Evolution roadmap of O-RAN security standards with 5G coinciding with each releases' safeguards' and up-coming planning.
Analysis of:
Threats and their protection measures of network interfaces in 5G system.
GSMA NESAS/SCAS 3GPP security assurance and test case specifications for virtualized gNB.
Security in Open vRAN.
Secure communications between the CNFs.
Interfaces description from 3GPP model as well newly introduced O-RAN protocols among which Non/Near-RT RIC and O2 interfaces being currently work in-progress.
Best security practices for CNF security:
Layered-block of several security in layers from infrastructure, Kubernetes, container, and application.
Kubernetes security: to have authenticated and authorized access into its control plane, securing data at the Rest level,
Containers security: across all stages and to avoid being noisy neighbors.
Disaggregation of key security differentiators between the traditional RAN and O-RAN.
Various ways the vDU and vCUs can expose threats to the front haul, mid-haul, and back-haul.

## Slide 80: Presentation 6: NIST Publication SP800-190. A container security guide. Presenter: John Morello from Palo Alto
Highlights:
SP800-190 covers: Threats and counter-measures through multiple layers of the stack, best practices around protecting the virtual machines and hosts applicable in the container world, fundamentals around vulnerability management and secure configuration.
Containers allow minimal host operating system reduces attack surface, evaluation of pre-deployment images, and look for vulnerabilities prior to production deployment.
Designed to be single-purpose focused entities that should maintain their same state throughout their lifecycle; the consistency allows security to be done in a more autonomous manner by creating a model by observing containers at the beginning of a life cycle.
Toolchain current state for containers can identify the artifacts contained within the container environment using images. Various tools are offered in the industry to do the software component analysis of these artifacts such as:
  Constant checks for vulnerabilities or security rule violations are performed in the build time while building the software.
  Check the distribution and deployment time for any mentioned vulnerabilities exist.
  Diversity and options in various tools offer how to store your code, conduct a build job, various ways of how to do deployment.
  Threshold for critical vulnerabilities check. In this case if there are vulnerabilities found beyond the set limit, the software is sent back to the vendor for control check.
For hybrid environment with virtual machines and container images:
  Virtual machines has less standardization around machine image formats.
  Disk image size for VM is found in GBs vs container images are in MBs.
  Large image sizes are not practical for easy transfer or image evaluation with build process.
  Containers provide the opportunity to potentially be more secure because of the efficiency that they provide making them secure and reliable.
  A hypervisor provides a greater degree of separation between individual entities that run above it than a container run-time does.
    A hypervisor allocate different tenants on a physical server using virtualization. Each of these tenant or virtualized OS may utilize containerization on top of this virtualized layer. In summary: a hypervisor is a hardware; a container run-time is an os layer.
  With most deployments being hybrid these days, the decision is to target the desired security dimension and then leverage the strengths of both layers in a customized order to get the solution with maximum advantage.
Greatest level of threat exists at the software application layer that is run on top and not as much on the underlying infrastructure running beneath.
  In the paper, it is recommended to group the applications by cluster levels of sensitivity, such as low, medium, and high criticality.
  Clusters are then separate from each other using hypervisor to avoid container escape or leakage using this isolation of hypervisor.
The best practices offered are generic and are applicable between all environments and networks.
  Some of the recommended check offs for infrastructure as a code, policies to not expose ssh to the outer world.
  More research to be done by the workgroup on finding various security templates.

## Slide 81: Presentation 7: ZTA for Secure 5G Cloud Deployments Presenter: Scott Poretsky, MSEE, CISSP, Director of Security MANA Network Product Solutions
Highlights:
Terminologies:
  Zero Trust - A concept that eliminates trust in digital systems based on the principal that no network user, packet, interface, or device should be trusted.
  Zero Trust Network Access (ZTNA) - Traditional perimeter security ensuring existence of authorization and authentication to gain remote access into a network or remote application. An IT security solution that provides secure remote access to an organization's applications, data, and services.
  Zero Trust Architecture (ZTA) - A plan (NIST 800-207) to be applied across any digital system. ZTA introduces the concept of perimeter less security and assumes that the adversary is already inside the network and moving laterally, according to CISA. ZTA includes ZTNA.
  Two definitions of ZTA for cloud deployments:
  NIST SP 800-207 - Introduces perimeter-less security. Based upon the principal that there is no implicit trust granted to an asset based upon ownership, physical location, or network location. This impacts the traditional way of securing the ORAN.
  CISA - An extension of ZTA and assumes that the adversary is already inside the network meaning we must protect the data as if the threat actor is already inside and can move laterally. (Protection is required for data in rest, data in motion as well data workloads to detect any suspicious movements.)
  USG Progression to ZTA in the 5G Cloud and various timelines:
  NIST SP 800-207 established in 2020 introduced 7 tenants.
  Solar-winds in 2020 lead to executive order in the White house EA 14028 calling on agencies to work on ZTA based on NIST establishment.
  CISA published its Cloud Security Technical Reference Architecture
  CISA Zero Trust Maturity Model containing 5 pillars
  OMB Zero Trust Cybersecurity Principles
  CISA Security Guidance for 5G cloud Infrastructure
  Log4j
  CISA Cloud Security Technical Reference Architecture highlights the connection between the cloud and ZTA.
  Being in cloud does not reciprocate to having a ZTA. Cloud services lets you enable the zero trust because the distributed nature of cloud necessitates additional configuration and management support in order to achieve the kind of security.
  CISA modernize its current cybersecurity programs, services, and capabilities to be fully functional with cloud-computing environments with ZTA.
  Telecommunication is one of the critical infrastructure categories for cloud security posture management oversees.
  ZTA can be very expansive and expensive making ZTA a long-term goal to strive towards while maintaining a risk-based analysis to your risk-based tolerance in a phased approach.
  In-parallel to protecting the inside of the cloud from internal thread actors, equal emphasis is needed to protect the resources themselves.
  CISA Security Guidance for 5G Cloud Infrastructures
  Primary highlights in regard to the 5G:
    Cloud-native 5G is a lucrative target for cyber threat actors
    In a hybrid or public cloud deployment, the MNO is accountable for the security posture of the deployment and apply a risk-based analysis.
    It is critical to continuously monitor for evidence of exploitation and adversarial lateral movement within 5G cloud deployments.
    This infrastructure offers four volumes of guidance and four security domains separately.
  3GPP 5G security are not zero trust architecture but several of the security points align with NIST 7 tenets of ZTA.
  ZTA in O-RAN is being applied to all work items and is covered as part of the NIST SP 800-207.

## Slide 82: Presentation 8: 5G Slice Creation: Design and Run Time Presenter: Leo Popokh, Ph.D., HPE Sr. Distinguished Technologist, Chief Technologist - HPE Communications Technology Group
Highlights:
5G network security from the end-user perspective, can be seen both ways - inside-out or outside-in. Focusing from inside-out includes:
  Telecommunications standardization process for secure protocols, algorithms, storage, 3gpp standards for 5G slice creation, standards for network function modeling.
  Vendor product development process to secure hardware and software components, secure the development process, version control and secure software update.
  Deployment process for solid network design with security and resilience, configuration of security parameters, hardening.
  Operation process to secure procedures such as, segregation of duties, use of least privilege and logging; monitoring the security performance, vulnerability management and detection of attacks; response and recovery post breach.
than access - it is UE with 5G serviListed table of various security threats in 5G with target elements in the network mapped to the effected technology and security.
5G deployment is more ce, radio access and network, transport network, core services, and slices.
  Horizontal and vertical security in 5G includes the system wide security at the network, slicing, and application level (includes the physical and infrastructure layers).
5G network slice eMBB slice example -
  At the physical layer, impacted technologies include 5G core hardware resources; radio hardware resources, such as towers, distributed units, central units; on-prem edge hardware; edge data centers; IOT devices; and power that can be compromised.
  At the virtual layer includes the hypervisor, open-stack, open-shift platform.
  Slices can be shared and dedicated for single user or for different users. They can be shared implying some of the network functions between multiple users.
Three main elements considered in the e2e slice creation infra management are: security management, security functions, and trust anchoring.
Espionage at the RAN vs core networks:
  RAN and transport & edge it can lead to the power-shell outages. RAN despite having a large number of radio access points distributed geographically, the risk can be mitigated by network segmentation. By design, the radio networks are encrypted and minimizing the exploitation.
  Even though core network represents a smaller portion of the overall network, a security breach here represents the highest security risk due to the presence of all subscribers' data. Compromise at the core network can cause a full outage with fully compromised network.
Discussion of Tier-1 use case to attain better understanding of how a slice is created, slice design, run-time of the slice, how the design is propagated, secure SSO, and R-back.

## Slide 83: Appendix

## Slide 84: Working Group 3: Methodology
Industry SME presentations
Standards bodies and industry associations (GSMA, CTIA, ETSI, 3GPP, NIST, ISO)
Individual contributor research gathered by Working Group members
Academic papers
Bi-weekly workgroup member meetings

## Slide 85: Discussion
WG3: Co-chairs
Micaela Giuhat, Microsoft
John Roese, Dell
WG3: Leveraging Virtualization Technology to Promote Secure, Reliable 5G Networks

## Slide 86: Presentation
WG4: Co-chairs
Mary Boyd, Intrado
Mark Reddish, APCO
WG4: 911 Service Over Wi-Fi

## Slide 87: Working Group 4: 911 Service Over Wi-Fi
September 21, 2022
Co-chairs:
Mary Boyd, Intrado Life & Safety
Mark Reddish, APCO
FCC Liaison: Rasoul Safavian

## Slide 88: Working Group 4: Background
The Chairwoman of the FCC directs CSRIC VIII to explore the public safety benefits, technical feasibility, and cost of options for making Wi-Fi access points and/or unlicensed spectrum available to the public to facilitate access to 911 services. The ubiquitous nature of Wi-Fi access points suggests that, in the long term, various Wi-Fi solutions could be added to the “toolbox” of 911 connectivity options available to consumers, Public Safety Answering Points (PSAPs), and communications providers, and could complement the broader transition to an IP-based Next Generation 911 environment.

## Slide 89: Working Group 4: Objectives
Bring industry stakeholders together to examine a range of technical issues with the goal of promoting consensus in the Wi-Fi ecosystem to support reliable 911 services (voice and text) under normal conditions and when catastrophic events disrupt mobile service. The primary focus will be to:
examine and report on security issues including authentication and access control protocols, solutions to automatically activate Wi-Fi Calling on eligible mobile devices, when necessary;
automatically determining the 911 caller location and call routing issues, 911 call prioritization, identifying missing standards, and timelines and costs for implementing 911 over Wi-Fi solutions.

## Slide 90
Working Group 4: Members
  *Also a CSRIC VIII Member
Brandon Abley,* National Emergency Number Association
Rob Alderfer,* Charter Communications
Mark Annas,* City of Riverside Fire Department, OEM
Michael Bergman,* Consumer Technology Association
Wade Buckner,* International Association of Fire Chiefs
Kirk Burroughs, Apple
Chinmay Dhodapkar, Google LLC
Stephen Edge, Qualcomm Technologies, Inc.
Katherine Elkins,* NHTSA
Harold Feld,* Public Knowledge
Fred Frantz, ANDRO Computational Solutions
Mark Gibson, CommScope
James D. Goerke, Texas 9-1-1 Alliance
Jeanna M. Green, T-Mobile
Kevin Green, Somos, Inc.
Mark Grubb, CISA
Mark Hess,* Comcast Corporation
Craig Hodan,* National Weather Service/NOAA
Everett Kaneshige,* NATOA
Robert Kubik, Samsung Electronics America
William 'Andy' Leneweaver, Washington State Military Department
Jason Lish,* Lumen Technologies, Inc.
William Mikucki, Comtech Telecommunications
Susan Miller,* ATIS
Charles (“Peter”) Musgrove, AT&T, Inc.
Theresa Reese, Ericsson
Travis Reutter,* ACA Connects- America's Communications Association
Charlie Sasser, National Association of State Technology Directors
Tim Schram,* NARUC
Sean Scott,* SecuLore Solutions
Malcolm Smith, Cisco Systems, Inc.
Stuart Strickland, Hewlett Packard Enterprise
Jeff Torres, Verizon Communications
Steve Watkins,* Cox Communications
Jeffrey Wittek, Motorola Solutions
Co-chairs: Mary Boyd,* Intrado
Mark Reddish,* APCO
FCC Liaison: Rasoul Safavian

## Slide 91
Working Group 4: Alternates*
* Alternates are not a member of the Working Group and may not vote.
  Chris Anderson, Lumen Technologies, Inc.
  Carol Ansley, Cox Communications
  Scott Blue, Cisco
  Tom Breen, SecuLore Solutions
  Matthew Chappell, Cox Communications
  Justen Davis, Somos, Inc.
  Nicholas Garcia, Public Knowledge
  J. David Grossman, CTA
  Michael Hooker, T-Mobile
  Brian Hurley, ACA Connects
  Christian Militeau, ATIS
  Darrin Morkunas, Intrado
  James B. Ramsay, NARUC
  Praveen Srivastava, Charter Communications
  Megan Stapleton, Comtech Telecommunications
  Brian Tegtmeyer, NHTSA
  Peter Thornycroft, Hewlett Packard Enterprise
  Alison Venable, APCO

## Slide 92: Working Group 4: Deliverables/Schedule
Sub-Teams established:
  Technical Feasibility (Active)
  Public Safety Benefits (Active)
  Cost (Awaiting outcomes of Technology & Benefits)
Meeting Schedules:
  Bi-Weekly (Full WG)
  Weekly / Bi-Weekly (Sub-Teams)
Baseline Report – In draft
Final Report on 911 Service over Wi-Fi, March 2023

## Slide 93: Working Group 4: Samples of Anticipated Report
Completed
  Framework for report contributions
  Framework for use case analysis
  Background information on 911 over Wi-Fi and public safety benefits
  Analysis of current network architectures / emergency call flow
  Outline of current and potential 911 over Wi-Fi use cases
  Use case analysis (partial)
In progress
  Additional use case analyses
  Recommendations

## Slide 94: Working Group 4: Next Steps
Weekly & bi-weekly meetings continue
Considering an in-person meeting
Continuing development of report contributions
On track for March 2023 completion

## Slide 95: Discussion
WG4: Co-chairs
Mary Boyd, Intrado
Mark Reddish, APCO
WG4: 911 Service Over Wi-Fi

## Slide 96: Presentation
WG6: Co-chairs
Farrokh Khatibi, Qualcomm Francisco Sanchez, SBA
WG6: Leveraging Mobile Device Applications and Firmware to Enhance WEA

## Slide 97: Working Group 6: Leveraging Mobile Device Applications and Firmware to Enhance Wireless Emergency Alerts
Co-chairs:
  Farrokh Khatibi, Qualcomm Technologies, Inc.
  Francisco Sanchez, U.S. Small Business Administration (SBA)
FCC Liaison: James Wiley and Tara Shostek
September 21, 2022

## Slide 98: Working Group 6: Background
The Chairwoman of the FCC directs CSRIC VIII to identify the software or functional requirements necessary to allow Wireless Emergency Alerts (WEA) software to pull capabilities from other mobile device applications and firmware to enhance the presentation of WEA alert messages. When WEA launched, mobile device manufacturers in collaboration with Commercial Mobile Service Providers that participate in WEA created specific programming procedures and rules for allowing their WEA applications to access and retrieve WEA messages. These programming procedures and rules are not available to third-party developers and do not currently allow the WEA software to interface with other mobile device functionality. This policy protects consumer privacy and the integrity of WEA messages, but also prevents WEA from leveraging many mobile device capabilities that could make WEA’s presentation of emergency information to the public more effective. To provide just two examples, researchers have found that allowing WEA to leverage the mapping capabilities of popular smartphone applications could reduce the amount of time the public spends trying to confirm that an emergency alert is relevant to them before taking action to protect their lives and property. Mobile devices also often contain a suite of accessibility features that, if leveraged in the WEA context, could make the emergency information that WEA messages contain more accessible to individuals with access and functional needs.

## Slide 99: Working Group 6: Objectives
To define an Application Programming Interface (API) to enable mobile device capabilities that could make WEA’s presentation of emergency information to the public more effective, including any features necessary to continue to secure WEA messages and protect consumer privacy. In addition to technical issues, CSRIC VIII should also identify any resource constraints or procedural issues that could affect the timely deployment of this Application Programming Interface and recommend appropriate mitigations.

## Slide 100: Working Group 6: Deliverables/Schedule
New Additional Deliverable:
Report on WEA Performance Reporting, December 2022
Report on WEA Application Programming Interface, March 2023

## Slide 101: Working Group 6: Members
FCC Liaison: James Wiley
Tara.Shostek
  *Also a CSRIC Member
Co-chairs: Farrokh Khatibi,* Qualcomm
Francisco Sanchez,* U.S. Small Business Administration (SBA)
Mark Annas,* City of Riverside Fire Department, OEM
Rebecca Baudendistel, NYC Emergency Management
Terri Brooks, T-Mobile
Wade Buckner,* International Association of Fire Chiefs
Kirk Burroughs, Apple
Brian K. Daly,* AT&T, Inc.
Harold Feld,* Public Knowledge
Craig Fugate,* America’s Public Television Stations
Michael Gerber, National Weather Service/NOAA
Dana Golub,* Public Broadcasting Service
Stephen Guiwits, US Geological Survey
Mark Hess,* Comcast Corporation
Antwane Johnson,* FEMA
Robert Kubik, Samsung Electronics America
Jennifer Lazo, City of Los Angeles Emergency Management Dept.
John Marinho, CTIA
Susan Miller,* ATIS
Krisztina Pusok,* American Consumer Institute
Matthew Straeb, Global Security Systems, LLC
Peter Tomczak,* FirstNet Authority
Dara Ung, Comtech Telecommunications Corp.
Larry Walke, National Association for Broadcasters
Steve Watkins,* Cox Communications
Chia-Kaung (Jack) Yu, Google LLC

## Slide 102: Working Group 6: Alternates*
* Alternates are not a member of the Working Group and may not vote.
  Tim Dunn, T-Mobile
  Nicholas Garcia, Public Knowledge
  Kevin Green, FirstNet Authority
  Al Kenyon, FEMA
  Edward Longe, American Consumer Institute
  Charles (“Peter”) Musgrove, ATIS
  Peter Scott, PBS

## Slide 103: Working Group 6: Status
Working Group Membership: Finalized
Working Group Meetings
  Weekly conference calls, with additional calls as needed
Document Library Established (ATIS Workspace)
  Contributions / Reference Documents / Calendars

## Slide 104: Working Group 6: Status
Reviewed existing WEA parameters available in the handset.
Reviewed Application Programming Interface (API) in the handset for Android and iOS Operating Systems.
Compiling a list of relevant use cases and analyzing them to determine which ones:
  could be supported by exposing existing WEA parameters to secure applications;
  may require enhancements to the existing WEA (i.e., new parameters required);
  may require major changes to the existing WEA, require alternative alerting techniques, or they are beyond the scope of WEA;
  may require standards, policy, and/or legislative changes.
Some use cases are outside the scope of CSRIC VIII WG6, but will be included in the report for future consideration.
Updating the draft Reports.

## Slide 105: Working Group 6: Status
At the request of the FCC, WG6 has agreed to accelerate WEA Performance Reporting use case for a new WG6 Report, due by the December CSRIC meeting.

## Slide 106: Working Group 6: Next Steps
Conduct routine weekly conference calls
  Continue to analyze use cases
  Develop new Recommendations
  Update the draft reports
Provide periodic status updates to Steering Committee and Council

## Slide 107: Discussion
WG6: Co-chairs
Farrokh Khatibi, Qualcomm Francisco Sanchez, SBA
WG6: Leveraging Mobile Device Applications and Firmware to Enhance WEA

## Slide 108: Closing Remarks
CSRIC VIII Co-chair
Billy Bob Brown, CISA

## Slide 109: Adjourn Meeting Suzon Cameron, DFO

## Slide 110: NEXT CSRIC VIII MEETING December 15, 2022 at 1:00 pm EST