## Slide 1: Sixth Meeting of THE COMMUNICATIONS SECURITY, RELIABILITY, AND INTEROPERABILITY COUNCIL VIII
December 15, 2022

## Slide 2: Open Meeting & Welcome Suzon Cameron, DFO

## Slide 3: Opening Remarks
PSHSB Chief
Debra Jordan, FCC

## Slide 4: Opening Remarks
CSRIC VIII Co-chair
Nasrin Rezai, Verizon

## Slide 5: Presentation
WG2: Co-chairs
Mike Barnes, Mavenir
George Woodward, RWA
Report on Challenges to the Development of ORAN Technology and Recommendations on How to Overcome Them

## Slide 6: Working Group 2: Promoting Security, Reliability, and Interoperability of Open Radio Access Network Equipment
December 15, 2022
Co-chairs:
Mike Barnes, Mavenir
George Woodward, RWA
FCC Liaison: Zenji Nakazawa

## Slide 7: Working Group 2: Background
The Chairwoman of the FCC directs CSRIC VIII to provide recommendations to advance security, reliability, and interoperability of Open Radio Access Network (ORAN) equipment in the United States and what new efforts can be undertaken to support secure and interoperable ORAN design and deployment.
The Radio Access Network (RAN) is the final link between the network and the phone. It includes the antennae on towers, buildings, and in stadiums, plus the base stations. When a consumer makes a call or connects to a remote server, the antenna transmits and receives signals to and from the consumer’s mobile phone or other handheld device. The signal is then digitalized in the RAN base station and connected into the network.
The introduction of ORAN enables mobile network operators to use equipment from multiple vendors and still ensure interoperability.

## Slide 8: Working Group 2: Objectives
CSRIC has previously considered security risks in emerging 5G networks.
CSRIC VIII builds on this work and expands it as one part of its exploration of the development and deployment challenges facing ORAN technology, including the extent Open RAN technology may increase the threat attack surface and how best to mitigate such security challenges.
Further, CSRIC VIII considers how the FCC can support the goals of developing and deploying secure, open and interoperable networks when the FCC participates in standards-setting bodies like 3GPP and the Alliance for Telecommunications Industry Solutions.

## Slide 9
Working Group 2: Members
  *Also a CSRIC VIII Member
Rob Alderfer,* Charter Communications
Robert Dew, CISA
Marla Dowell,* NIST
Andrew L. Drozd,* ANDRO Computational Solutions
Russ Gyurek, Cisco Systems, Inc.
Javed Khan,* Altiostar Networks
Michael Loushine, AT&T, Inc.
Jennifer Manner,* Hughes Communications
Martin McGrath, Nokia
Jack Nasielski, Qualcomm Technologies, Inc.
Scott Poretsky, Ericsson
Vishwanath Ramamurthi, Verizon Communications
Stefan Saroiu, Microsoft Corporation
Tom Sawanobori,* CTIA
Tim Schram,* NARUC
Nick Solano, Qcommunications, LLC
Eric Tamarkin, Samsung Electronics America
Jean Trakinat, T-Mobile
Claire Vishik,* Intel
Henry Young,* BSA | The Software Alliance
Tim May,* NTIA
FCC Liaison: Zenji Nakazawa
Co-chairs: Mike Barnes,* Mavenir
George Woodward,* RWA

## Slide 10
Working Group 2: Alternates*
* Alternates are not a member of the Working Group and may not vote.
  Reza Arefi, Intel
  Afeite Dadja, CTIA
  Brian Daly, AT&T
  Heidi Obermeyer, BSA | The Software Alliance
  Anand Palanigounder, Qualcomm
  Sanil Rama Chandran, Samsung
  James B. Ramsay, NARUC
  Nancy Shemwell, Rural Wireless Association
  Lakhbir Singh, Charter Communications
  Matthew Sneed, Hughes Communications
  Ryan Stokes, Rural Wireless Association
  Lap Tse, Verizon Communications
  Timothy O. Woods, ANDRO Computational Solutions

## Slide 11: Working Group 2: Deliverable/Schedule
Deliverable: Report on the Challenges to the Development of ORAN Technology and Recommendations on How to Overcome Them
  First WG2 meeting December, 2021
  First Draft completed June, 2022
  Final Review started September, 2022
  Report Complete November, 2022
Submitting the report today for full Council consideration

## Slide 12: Report Structure
Executive Summary
Background
  Cellular Radio Access Networks
  Open RAN Ecosystem
  O-RAN
  Open RAN Supply Chain Security Risks
Analysis
  O-RAN Architecture Security
  Secure Open RAN Software Development
  Operations
  Supply Chain
  Policy
Recommendations to the FCC and Industry
Conclusion

## Slide 13: Report Methodology
The following areas were studied, with an emphasis on security, reliability, and interoperability:
  O-RAN Architecture
  Open RAN Cloud Infrastructure
  Open RAN Deployments
  Open RAN Operations
  Open RAN Supply Chain
  Open RAN Software Development Process
  Note: In this report, the term “O-RAN” refers to the O-RAN Alliance, while the term “Open RAN” applies to all Open RAN technologies.

## Slide 14: Executive Summary - Approach
Open RAN enhances the 5G mobile network by evolving the RAN architecture with open interoperable interfaces, virtualization, and big data and AI-enabled intelligence. Open RAN includes O-RAN, Virtual RAN (vRAN), Cloud RAN, and other technologies. The introduction of Open RAN enables mobile network operators to use equipment from multiple vendors while ensuring interoperability.
This report describes Open RAN architectures, security considerations, and challenges to the development of a secure Open RAN ecosystem. These challenges include the growing maturity of the technology, the desire to grow the pool of vendor solutions, the need for multi-vendor solution integration, and a variety of specific technical choices to be made as Open RAN systems develop.
This report provides:
Background on Open RAN technology, ecosystem, supply chain and deployment.
Analysis of Open RAN architecture and cloud infrastructure, software development, operations and supply chain, including recommendations in each area.
Recommendations to the FCC and Industry, including proposed future areas of investigation.

## Slide 15: Executive Summary - Analysis
Security concerns exist in both Open RAN and closed proprietary RAN.
Open RAN application, open source software, supply chain, and zero trust concerns are consistent with those from the Information and Communications Technology (ICT) sector.
Open RAN utilizes existing 5G Core network technologies including multi-vendor core network functions and 5G cloud infrastructures.
Open RAN will benefit by adopting ICT and 5G best practices for secure, reliable and interoperable deploy & operation.
Open RAN brings new capabilities and concerns with the introduction of xApps/rApps application frameworks, AI/ML technology, and the O-RAN Alliance defined Open Fronthaul network connecting base stations and radios with real-time performance requirements. Some of these concerns are shared with the ICT sector.
Both Open and proprietary fronthaul solutions are challenged to balance the security requirements with performance and cost considerations.
With the continued evolution of Open RAN, security and reliability continues to be addressed by the appropriate groups such as O-RAN Alliance and ICT and 3GPP standards evolution.
Note: This analysis is consistent with the conclusions from the Enduring Security Framework (ESF) report on “Open RAN Security Considerations”

## Slide 16: Background: Technology Overview
Cellular Radio Access Networks
Open RAN Ecosystem
O-RAN Alliance
Open RAN Supply Chain Security Risks
Issues facing Open RAN deployment in U.S.

## Slide 17: Analysis: Open RAN Architecture Security
Securing Management and Orchestration
RAN Intelligent Controllers (RICs)
Open Fronthaul Interface
O-Cloud
O-RAN Coexistence Orchestration to Mitigate Security Vulnerabilities in Multi-RAT Environments
Broader Security Considerations of Open RAN
Threats to Open RAN Architecture

## Slide 18: Analysis: Secure Open RAN Software Development
Evolution of Secure Software Development
Secure Development Phases
NIST Secure Software Development Framework (SSDF)
O-RAN Software Community (OSC)

## Slide 19: Analysis: Operations
Challenges in multi-vendor RAN environment
Challenges for Distributed Far-Edge
Training
Compliance

## Slide 20: Analysis: Supply Chain
Observations about the Open RAN Supply Chain
Current RAN Supply Chains
Telecommunications Supply Chain
Elements of software/firmware (SBOM and software inventory)
Open-source Software (OSS)

## Slide 21: Recommendations
    CSRIC VIII identified seven (7) recommendations to the FCC and twenty-four (24) recommendations to industry.
    Key recommendations are summarized in the following two slides, followed by the full list of recommendations.

## Slide 22: Key Recommendations to the FCC
Work with the Commerce Department, National Science Foundation and other agencies responsible for STEM workforce development, and the Departments of Homeland Security and State to support US workforce training needs and skilled labor immigration to address skills gaps which impede Open RAN development, and with industry to establish programs that facilitate a talent pipeline from HBCUs.
Promote global economies of scale in the Open RAN ecosystem through industry-led, collaborative standards and interoperability efforts, and encourage US industry leadership in standards via clear exemptions. To this end, consult with the Departments of Commerce, State, Treasury, and Defense as the Administration considers export controls or other sanctions that may impact Open RAN standards development and interoperability.
Accelerate Open RAN ecosystem growth through incentives including consulting with the Commerce Department on the Public Wireless Supply Chain Innovation Fund and other programs for: 1) R&D of Open RAN hardware and software; 2) multi-vendor interoperability and system integration, such as the OTIC program; 3) RIC Application development to drive Open RAN system performance, visibility, and automation; 4) Technology enablers such as semiconductor innovation and integration with diverse transport networks.

## Slide 23: Key Recommendations to Industry
Work within ATIS to establish an Open RAN focus group for National Security and Emergency Preparedness, Public Safety and Emergency Services.
Base Open RAN implementations on the principles of Zero Trust Architecture (ZTA) and a Secure Software Development Life Cycle (SDLC).
Implement Open RAN architecture defenses and O-RAN Alliance specifications to prevent Adversarial Machine Learning (AML) attacks.
Apply the O-RAN Alliance test specifications as applicable, and complete the O-RAN specifications to ensure a baseline exists for Interoperability testing.
Facilitate the evaluation of Open RAN technologies for interoperability, performance, and security for different use cases and deployment scenarios.

## Slide 24: Recommendations – Full List
Recommendation-Arch-FCC-1: CSRIC VIII recommends future CSRICs consider further CSRIC work on the Quantum Computer threat.
Recommendation-SWDev-FCC-1: CSRIC VIII recommends that the FCC facilitate the establishment of a collaborative national 5G Open RAN emulation environment that is available to industry, academia, and government to evaluate and identify zero day attacks. For example, this could be accomplished by expanding the NIST NCCoE or encouraging utilization of the United States based Open Test and Interoperability Center (OTIC).
Recommendation-Ops-FCC-1: CSRIC VIII recommends that the FCC work with the Department of Commerce, National Science Foundation, National Academies, and other agencies that have responsibility for STEM workforce development, as well as the Departments of Homeland Security and State on visa and skilled worker entry requirements to support workforce training needs and skilled labor immigration to address US labor skills gaps that may impede the development of Open RAN. Furthermore, it is recommended that the FCC work with industry to establish programs that facilitate a talent pipeline from HBCUs.
Recommendation-Policy-FCC-1: CSRIC VIII recommends that the FCC encourages innovation and the development of Open RAN solutions that address market-driven use cases, rather than mandating Open RAN requirements.
Recommendation-Policy-FCC-2: CSRIC VIII recommends that the FCC promotes global economies of scale in the Open RAN ecosystem through industry-led, collaborative standards and interoperability efforts, and encourage US industry leadership in standards via clear exemptions from export controls for these standards efforts. To this end, CSRIC VIII recommends that the FCC should consult with the Departments of Commerce, State, Treasury, and Defense as the Administration considers export controls or other sanctions that may impact Open RAN standards development and interoperability.

## Slide 25: Recommendations – Full List
Recommendation-Policy-FCC-3: CSRIC VIII recommends the FCC accelerate the growth of the Open RAN ecosystem through incentives, including consulting with the Commerce Department as it makes funding available through the Public Wireless Supply Chain Innovation Fund, as well as other available programs, toward the following purposes: 1) Research and development of Open RAN hardware and software solutions; 2) multi-vendor interoperability and system integration efforts, such as the OTIC program as well as such efforts undertaken in MNO and Vendor Labs ; 3) Application development for the RIC to drive Open RAN system performance, visibility, and automation; and, 4) Technologies that enable Open RAN ecosystem development and growth, including semiconductor innovation and integration with diverse transport networks.
Recommendation-Policy-FCC-4: CSRIC VIII recommends that the FCC not create new certification requirements on Open RAN products beyond current and existing requirements for RAN equipment. See related Recommendation-Ops-Indust-1.

## Slide 26: Recommendations – Full List
Recommendation-Arch-Indust-1: CSRIC VIII recommends that CSRIC VII recommendations for securing 5G SA networks should apply to Open RAN.
Recommendation-Arch-Indust-2: CSRIC VIII recommends that the CSRIC VI recommendations for securely consuming open-source software for deployment in 5G production networks should apply to Open RAN.
Recommendation-Arch-Indust-3: CSRIC VIII recommends that the CSRIC VI recommendations for digital signing of production software should apply to Open RAN workloads, including network functions and applications.
Recommendation-Arch-Indust-4: CSRIC VIII recommends that ethernet based Front Haul networks be segmented to isolate FH traffic from other traffic flows and that port based authentication be used to enable authorization of network elements attached to the FH network.
Recommendation-Arch-Indust-5: CSRIC VIII recommends that secure protocols providing mutual authentication be used when deploying RUs with ethernet based FH in US production networks.
Recommendation-Arch-Indust-6: CSRIC VIII recommends that IEEE 802.1X Port-based Network Access Control be implemented for all Network Elements that connect to the Open FH network deployed in hybrid mode.
Recommendation-Arch-Indust-7: CSRIC VIII recommends that RICs are enabled with conflict mitigation capability when deploying Open RAN with 3rd-party rApps or xApps.
Recommendation-Arch-Indust-8: CSRIC VIII recommends that the US telecommunications industry should establish test specifications for xApps and rApps to ensure secure integration into the RIC platforms and protection of sensitive data.

## Slide 27: Recommendations – Full List
Recommendation-Arch-Indust-9: CSRIC VIII recommends that separation and isolation of applications (i.e., xApps/rApps) should be built-in to reduce the possibility of further compromise to other Open RAN components or applications if those applications become compromised.
Recommendation-Arch-Indust-10: CSRIC VIII recommends that Open RAN software be deployed on secure server hardware. The credentials and keys used as part of the Open RAN software should be encrypted and stored securely.
Recommendation-Arch-Indust-11: CSRIC VIII recommends that US industry should drive evolution of Open RAN security specifications at the relevant standards bodies and industry consortia to align with the recommendations in this report.
Recommendation-Arch-Indust-12: CSRIC VIII recommends that Open RAN implementations should be based on the principles of Zero Trust Architecture (ZTA).
Recommendation-Arch-Indust-13: CSRIC VIII recommends that Open RAN products should follow the same processes used to certify equipment, to the extent they are used for priority communications for National Security and Emergency Preparedness (NS/EP), public safety and critical infrastructure.
Recommendation-Arch-Indust-14: CSRIC VIII recommends US industry to work within ATIS to establish an Open RAN focus group for NS/EP, Public Safety and Emergency Services.
Recommendation-Arch-Indust-15: CSRIC VIII recommends that Industry should assess the need for establishing a process for accreditation of independent test laboratories for Open RAN multi-vendor security, priority, interoperability and performance testing.

## Slide 28: Recommendations
Recommendation-Arch-Indust-16: CSRIC VIII recommends that Open RAN architectures implement defenses to prevent Adversarial Machine Learning (AML) attacks. Industry should work within the O-RAN Alliance to drive security specifications that mitigate AML attacks.
Recommendation- Arch-Indust-17: CSRIC VIII recommends that the MNO use secure boot based on hardware root of trust, with credentials securely stored (e.g., in an HSM), and software signing to establish an end to end chain of trust.
Recommendation-SWDev-Indust-1: CSRIC VIII recommends that the Open RAN ecosystem puts security at the core of the Software Development Life Cycle (SDLC) by utilizing best practices such as NIST DevSecOps, NIST SSDF, BSA Framework for Secure Software, or SAFECode.
Recommendation-Ops-Indust-1: CSRIC VIII recommends that industry determines the need for formal certifications of Open RAN solutions and the applicability of those certifications to the deployment and use cases.
Recommendation-Ops-Indust-2: CSRIC VIII recommends that all O-RAN stakeholders apply the O-RAN Alliance’s test specifications as applicable.
Recommendation-Supply-Indust-1: CSRIC VIII recommends that US O-RAN community members develop and complete the O-RAN specifications to ensure a baseline exists for Interoperability testing.

## Slide 29: Recommendations
Recommendation-Supply-Indust-2: CSRIC VIII recommends that industry facilitate the evaluation of Open RAN technologies for interoperability, performance, and security for different use cases and deployment scenarios.
Recommendation-Supply-Indust-3: CSRIC VIII recommends that optional fields, whose usage could potentially jeopardize interoperability, be minimized.
Recommendation-Supply-Indust-4: CSRIC VIII recommends that the Open RAN Industry adopts Software Bill of Materials (SBOMs), e.g., O-RAN Alliance Working Group 11 Security requirements.

## Slide 30: Conclusion
Concerns exist in both Open RAN and closed proprietary RAN. Open RAN security considerations with applications, open source software, supply chain, and zero trust are consistent with those from the Information and Communications Technology (ICT) sector, and Open RAN must implement the ICT best practices to address these concerns. Open RAN utilizes existing 5G Core network technologies including multi-vendor core network functions and 5G cloud infrastructures. Open RAN will benefit by adopting the ICT and 5G best practices to ensure secure, reliable and interoperable deployment and operation.
Open RAN brings new capabilities and concerns with the introduction of xApps/rApps application frameworks and AI/ML technology, and the O-RAN Alliance specified Open Fronthaul network connecting base stations and radios with real-time performance requirements. Some of these concerns are shared with the ICT sector, and both Open and proprietary fronthaul solutions are challenged to balance the security requirements with performance and cost considerations.
With the continued evolution of Open RAN, security and reliability continues to be addressed by the appropriate groups such as O-RAN Alliance and ICT and 3GPP standards evolution.
CSRIC recommends that the FCC and industry act on the recommendations identified in this report by leveraging existing best practices to address common concerns and implement new processes to mitigate new attack vectors.

## Slide 31: Discussion
WG2: Co-chairs
Mike Barnes, Mavenir
George Woodward, RWA
Report on Challenges to the Development of ORAN Technology and Recommendations on How to Overcome Them

## Slide 32: Call For Vote
WG2: Co-chairs
Mike Barnes, Mavenir
George Woodward, RWA
Report on Challenges to the Development of ORAN Technology and Recommendations on How to Overcome Them

## Slide 33: Presentation
WG3: Co-chairs
Micaela Giuhat, Microsoft
John Roese, Dell
Report on How Virtualization Technologies can be Used to Promote 5G Security and Reliability

## Slide 34: Working Group 3: Leveraging Virtualization Technology to Promote Secure, Reliable 5G Networks
Co-chairs:
Micaela Giuhat, Microsoft
John Roese, Dell
FCC Liaison: Jeff Goldthorp

## Slide 35: Milestones
Report on How Virtualization Technologies can be Used to Promote 5G Security and Reliability - December 2022
Report on Recommendation on the Role of the FCC in Promoting the Availability of Standards for More Secure, Reliable 5G Environment Through the Use of Virtualization Technology - June 2023

## Slide 36: Objective
This first report on How Virtualization Technologies can be Used to Promote 5G Security and Reliability, for CSRIC VIII will include recommendations on:
  Ways in which funding and non-funding methods can be deployed to promote virtualized environments that result in improved 5G security and reliability.
  Recommendations on ways to promote and overcome obstacles and increase 5G vendor diversity for virtualized systems including Distributed Unit (DU), Central Unit (CU), Radio Unit (RU) and Service Based Architecture (SBA).
  Best practices for reliability and interoperability by enabling the 5G ecosystem to be open and create interworking between small and large vendors in the same 5G system. These recommendations should also broadly focus on reducing the cost of entry for 5G and making it more accessible to smaller adopters of the technology.
  CSRIC VIII will also identify whether any additional work is needed from a broad landscape of IT, Cloud and Telecom standards and initiatives that virtualized 5G is dependent on.

## Slide 37
Marla Dowell,* NIST
Andrew L. Drozd,* ANDRO Computational Solutions
Bob Everson, Cisco Systems, Inc.
Michael Gallagher, Verizon Communications
Martin Goldberg,* National Security Agency
Javed Khan,* Altiostar Networks
Douglas Knisely, Qualcomm Technologies, Inc.
Jennifer Manner,* Hughes Communications
Serge Manning, T-Mobile
Timothy May, NTIA
Martin McGrath, Nokia
William Mikucki,* Comtech Telecommunications Corp.
Keith O’Brien, Palo Alto Networks
Jitendra Patel, AT&T, Inc.
Leo Popokh, ATIS
Scott Poretsky, Ericsson
Tom Sawanobori,* CTIA
Jane Shen, Mavenir
Paul Steinberg,* Motorola Solutions
Frank Suraci, CISA
Peter Tomczak,* FirstNet Authority
Claire Vishik,* Intel
Damien Whaley, Cox Communications
George Woodward, Rural Wireless Association
Working Group 3: Members
  FCC Liaison: Jeff Goldthorp *Also a CSRIC VIII Member
Co-chairs: Micaela Giuhat,* Microsoft
John Roese,* Dell

## Slide 38
  Reza Arefi, Intel
  Afeite Dadja, CTIA
  Kevin Green, FirstNet Authority
  Bryan Larish, Verizon Communications
  Doug Montgomery, NIST
  Vishwamitra Nandlall, Dell Technologies
  Stere Preda, Ericsson
  Rowland Shaw, Dell Technologies
  Matthew Sneed, Hughes Communications
  Megan Stapleton, Comtech Telecommunications Corp.
  Darrell Stogner, Motorola Solutions
  Ryan Stokes, Rural Wireless Association
  Richard Tenney, CISA
  Timothy Woods, ANDRO Computational Solutions
Working Group 3: Alternates*
* Alternates are not a member of the Working Group and may not vote.

## Slide 39: Working Group 3 Deliverables and Schedule
Scope and Methodology Agreement December 7th, 2021
Create list of SMEs and other industry bodies to be invited January 2022
Finish gathering of information June 2022
Create paper outline/sections Q2 2022
Assign individual contributors the different sections to be done Q3 2022
Collate, edit, finalize 1st paper December 2022
Start working on 2nd milestone 2nd Half 2022

## Slide 40: Methodology
Reviewed industry lessons learned from use of virtualization and increased vendor diversity in strengthening security, increasing competition, and creating a more secure supply chain.
Gathered insights and input from researchers, technologists, thought leaders and standards development organizations on availability of solutions, and technical issues to be addressed.
Performed an assessment of implementation best practices and reviewed results from test labs or real-life deployments around the world.
Performed comparison between virtualized and non-virtualized security vulnerabilities in a 5G network.
Identified issues to be addressed by the commission and provided high level recommendations on how best to support a secure diverse vendor ecosystem.
Provided in depth information on list of threats, mitigation, and 3GP SA3 Virtualization through Appendices B to D

## Slide 41: Document Structure
Chapter 3 Scope and premise for leveraging virtualization technology to promote secure, reliable 5G networks.
Chapter 4 The broad concept of virtualization as a practice.
Chapter 5 How virtualization is impacting 5G and its embrace by the network provider ecosystem.
Chapter 6 View on security and operating integrity when virtualizing a 5G network.
Chapter 7 Complexities introduced by the confluence of multiple industries, and standards practices
Chapter 8 Recommendations abstracted from deep technical insight to inform at a policy creation level.

## Slide 42: Summary of Recommendations
Intra governmental partnering: For the supply chain, consider ways to partner across the federal government to continue to incentivize digital solutions in 5G network deployments to mitigate supply chain risk. Also, to monitor and collaborate with other government agencies who have similar concerns and are undertaking proactive actions or developing tools relevant to The Communications Security, Reliability and Interoperability Council VIII Leveraging Virtualization Technology to Promote Secure, Reliable 5G Networks December 2022 the secure and successful application of virtualization and related technologies including Zero Trust.
Public and private sector partnering: Convene a virtualized 5G industry information sharing group comprised of experts from government, research, academia, service providers, and equipment providers. This syndicated development of common patterns and playbooks of migration could be convened and incented including driving standards development or product capabilities.
Overcoming obstacles and increasing vendor diversity: Industry should continue to use its existing processes for equipment certification and evaluate the need and relevance to establish a new certification for the deployment of network functions in virtualized environments.
To address best practices for reliability and interoperability by enabling the 5G ecosystem to be open and create interworking between small and large vendors in the same 5G system, it is recommended that both the FCC and NIST (including other U.S government agencies as necessary) develop consistent and co-branded guidance.
Skilling needed to support virtualized 5G networks: Build the Workforce for Cloud based 5G networks which will bring more diversity and innovation to the 5G and next generation wireless networks. Specifically, provide support in building and sustaining a leading talent pipeline which emphasizes Radio / RF and the crossover capabilities between the IT and Telecom domains

## Slide 43: Discussion
WG3: Co-chairs
Micaela Giuhat, Microsoft
John Roese, Dell
Report on How Virtualization Technologies can be Used to Promote 5G Security and Reliability

## Slide 44: Call For Vote
WG3: Co-chairs
Micaela Giuhat, Microsoft
John Roese, Dell
Report on How Virtualization Technologies can be Used to Promote 5G Security and Reliability

## Slide 45: Presentation
WG6: Co-chairs
Farrokh Khatibi, Qualcomm Francisco Sanchez, SBA
Report on WEA Performance Reporting

## Slide 46: Working Group 6: Leveraging Mobile Device Applications and Firmware to Enhance Wireless Emergency Alerts
Co-chairs:
  Farrokh Khatibi, Qualcomm Technologies, Inc.
  Francisco Sanchez, U.S. Small Business Administration (SBA)
FCC Liaison: James Wiley and Tara Shostek
December 15, 2022

## Slide 47: Working Group 6: Background
The Chairwoman of the FCC directs CSRIC VIII to identify the software or functional requirements necessary to allow Wireless Emergency Alerts (WEA) software to pull capabilities from other mobile device applications and firmware to enhance the presentation of WEA alert messages. When WEA launched, mobile device manufacturers in collaboration with Commercial Mobile Service Providers that participate in WEA created specific programming procedures and rules for allowing their WEA applications to access and retrieve WEA messages. These programming procedures and rules are not available to third-party developers and do not currently allow the WEA software to interface with other mobile device functionality. This policy protects consumer privacy and the integrity of WEA messages, but also prevents WEA from leveraging many mobile device capabilities that could make WEA’s presentation of emergency information to the public more effective. To provide just two examples, researchers have found that allowing WEA to leverage the mapping capabilities of popular smartphone applications could reduce the amount of time the public spends trying to confirm that an emergency alert is relevant to them before taking action to protect their lives and property. Mobile devices also often contain a suite of accessibility features that, if leveraged in the WEA context, could make the emergency information that WEA messages contain more accessible to individuals with access and functional needs.

## Slide 48: Working Group 6: Objectives
To define an Application Programming Interface (API) to enable mobile device capabilities that could make WEA’s presentation of emergency information to the public more effective, including any features necessary to continue to secure WEA messages and protect consumer privacy. In addition to technical issues, CSRIC VIII should also identify any resource constraints or procedural issues that could affect the timely deployment of this Application Programming Interface and recommend appropriate mitigations.

## Slide 49: Working Group 6: Deliverables/Schedule
Report on WEA Performance Reporting, December 2022
Report on WEA Application Programming Interface, March 2023

## Slide 50: Working Group 6: Members
FCC Liaisons: James Wiley
Tara.Shostek
  *Also a CSRIC Member
Co-chairs: Farrokh Khatibi,* Qualcomm
Francisco Sanchez,* U.S. Small Business Administration (SBA)
Mark Annas,* City of Riverside Fire Department, OEM
Rebecca Baudendistel, NYC Emergency Management
Terri Brooks, T-Mobile
Wade Buckner,* International Association of Fire Chiefs
Kirk Burroughs, Apple
Brian K. Daly,* AT&T, Inc.
Harold Feld,* Public Knowledge
Craig Fugate,* America’s Public Television Stations
Michael Gerber, National Weather Service/NOAA
Dana Golub,* Public Broadcasting Service
Stephen Guiwits, US Geological Survey
Mark Hess,* Comcast Corporation
Antwane Johnson,* FEMA
Robert Kubik, Samsung Electronics America
Jennifer Lazo, City of Los Angeles Emergency Management Dept.
John Marinho, CTIA
Susan Miller,* ATIS
Krisztina Pusok,* American Consumer Institute
Matthew Straeb, Global Security Systems, LLC
Peter Tomczak,* FirstNet Authority
Dara Ung, Comtech Telecommunications Corp.
Larry Walke, National Association for Broadcasters
Steve Watkins,* Cox Communications
Chia-Kaung (Jack) Yu, Google LLC
Editor: Terri Brooks

## Slide 51: Working Group 6: Alternates*
* Alternates are not a member of the Working Group and may not vote.
  Tim Dunn, T-Mobile
  Nicholas Garcia, Public Knowledge
  Kevin Green, FirstNet Authority
  Al Kenyon, FEMA
  Nathanael Scherer, American Consumer Institute
  Charles (“Peter”) Musgrove, ATIS
  Peter Scott, PBS

## Slide 52: Objective of the Report on WEA Performance Reporting
While WEA is a one-way broadcast service that is not designed to enable the collection of performance data, there is belief that having additional insights into WEA’s reliability, latency and accuracy, as indicators of how WEAs propagate in communities, may assist Alert Originators in planning alerts and build public confidence in receiving the relevant alert expeditiously.

## Slide 53: Wireless Emergency Alert System

## Slide 54: Definitions
Broadcast Area:
  Geographic area selected for the WEA broadcast.
Alert Area:
  Geographic area of the geometric shape defined by coordinates provided by the Alert Originator. This is the area to which the alert applies.
Broadcast Area
Alert Area

## Slide 55: Definitions
Accuracy | Number of devices inside the Alert Area which (including within 0.1 miles of the Alert Area boundary) presented the WEA divided by the total number of devices that presented the WEA.
Latency | Time between when the Alert Originator sends the WEA and the time that the WEA is presented on a device.
Reliability | Proportion of devices within the Alert Area (including within 0.1 miles of the Alert Area boundary) that received and appropriately processed (e.g., presented if appropriate based on user’s setting, location, etc.) the alert.
Performance Metrics

## Slide 56: Identified Needs as Provided by the Alert Originators Reliability
Reliability, defined as the proportion of devices within the Alert Area (including within 0.1 miles of the Alert Area boundary) that received and appropriately processed (e.g., presented if appropriate based on user’s setting, location, etc.) the alert, may also include information such as:
  The number of mobile devices that received the alert and presented it successfully.
  The number of mobile devices that received the alert but did not present it due to being outside the Alert Area.
  The number of mobile devices that received the alert, presented the alert by default due to location being unavailable (e.g., location services turned off).
  The number of mobile devices that received the alert but did not present due to the user’s mobile device settings (e.g., opted out of AMBER alerts).
  The number of all mobile devices that should have received the alert.

## Slide 57: Identified Needs as Provided by the Alert Originators Latency
Latency, defined as the time between when the Alert Originator sends the WEA and the time that the WEA is presented on a device, may also include intermediary timestamp information which includes:
  the time CAP alert is originated by an alert originator,
  the time the CAP alert is received at FEMA IPAWS,
  the time FEMA IPAWS delivers the WEA alert to each Participating CMSP,
  the time FEMA IPAWS delivers the WEA alert to PBS,
  the time that each Participating CMSP receives the alert at their CMSP Gateway,
  the times that each Participating CMSP starts broadcasting the WEA*,
  the time that PBS begins broadcasting the WEA,
  the time that the WEA is received at the mobile device, and
  the time that the WEA is presented to the user.
* During the standardization process the definition of “start of broadcasting” would need to be defined.

## Slide 58: Identified Needs as Provided by the Alert Originators Accuracy
Accuracy, defined as the number of devices inside the Alert Area which (including within 0.1 miles of the Alert Area boundary) presented the WEA divided by the total number of devices that presented the WEA, could also be characterized with information to include:
The distance outside the alert area where the WEA was presented
  Average distance outside the alert area
  Median distance outside the alert area
  Maximum distance outside the alert area
  Minimum distance outside the alert area

## Slide 59: Analysis
Three proposals were analyzed:
  State/Local WEA Test.
  Automated Performance Reporting from Opted-In Consumer Devices.
  Automated Reporting from Staged Devices.

## Slide 60: State/Local WEA Test
The State/Local WEA Test is required to be supported by CMSPs in the FCC’s 4th Report and Order, released in September 2016.
The FCC, FEMA, CMSPs, and state and local public safety agencies have carried out nationwide and localized alert tests since 2016, producing reports on capabilities and effectiveness of WEA.
The State/Local WEA Test capability allows for controlled testing done by the Alert Originators, with a known group of Test Participants at specified dates/times to enable reliable testing and analysis. This would allow for testing and building confidence of the end-to-end flow by the Alert Originator.

## Slide 61: State/Local WEA Test
Reliability
Reported by the Test Participant:
  Presentation of the alert based upon location of device/Test Participants for Ground Truth verification
  Service provider
  Device settings (S/L test on/off, Location on/off)
  Device Manufacturer, Model, and OS version (a TAC of the Handset would be ideal).
Latency
Reported by the Test Participant:
  Time of presentation on the handset
  Pertinent details if presentation was later than expected, such as surroundings (e.g., in an elevator) that may have influenced reception
Reported by the Alert Originator:
  Time the alert was initiated
Reported by FEMA:
  Time the alert was received
  Time the alert was sent to the CMSPs
Reported by the CMSP:
  Time the alert was received
  Time the alert was first broadcast
Accuracy
Reported by the Test Participant:
  Location at time of presentation (e.g., lat/long, civic address)
  Manufacturer/model/OS version (to determine DBGF capabilities)
  Device settings (S/L test on/off, Location on/off)
Reported by the Alert Originator:
  1) Alert Polygon Generated

## Slide 62: Automated Performance Reporting from Opted-In Consumer Devices
New automated reporting about WEA’s performance by WEA stakeholders may have the potential to provide additional insights, which may increase the confidence in the use of WEA. Reporting of WEA’s reliability, latency, and accuracy is proposed through the following steps:
  Consumer opt-in: Enabling device users to opt-in to the collection and sharing of WEA data, specifically for the purpose of determining metrics, with the understanding that this data will be anonymized at the collection point,
  Performance Metric Data Collection: WEA stakeholders collect message receipt and presentation and other performance-related data,
  Reporting the Performance Data: WEA stakeholder(s) sends the relevant parameters to a single data collection point for metric calculations, and
  Performance Data Availability: Enabling all stakeholder(s) (e.g., CMSPs, FEMA, Alert Originators) to have controlled access to this data.

## Slide 63: Automated Performance Reporting from Opted-In Consumer Devices
Reliability*
WEA Reliability calculations have the following challenges and limitations:
  Reliability calculations as previously defined cannot require a proportion to the total number of mobile devices in the Alert Area, because this is unknown, dynamic, and cannot be obtained.
  The number of devices for which users have opted into allowing performance reporting and are in the Alert Area will also not be known, and any given device may not receive and present the alert (e.g., radio anomaly, inside an elevator), and would subsequently not report it received the alert. This also will make the reliability metric unreliable.
* See Additional Perspectives in the Recommendations Slide

## Slide 64: Automated Performance Reporting from Opted-In Consumer Devices
Latency
From the Alert Originator:
  Date/timestamp of the origination of the WEA
From FEMA IPAWS:
  Date/Timestamp when the CAP message was received from the AO
  Date/Timestamp when the WEA message was delivered to each Participating CMSP
  Date/Timestamp when the WEA message was delivered to PBS
From PBS:
  Date/Timestamp when the WEA message was received from FEMA IPAWS
  Date/Timestamp when the WEA was broadcast by the PBS broadcast network
From each Participating CMSP:
  Date/Timestamp when the WEA message was received from FEMA IPAWS, or PBS
  Date/Timestamp when the WEA was first broadcast from the CMSP infrastructure
From the Mobile Device:
  Date/Timestamp of the receipt of the WEA
  Date/Timestamp of the presentation of the WEA, if presented

## Slide 65: Automated Performance Reporting from Opted-In Consumer Devices
Accuracy
WEA accuracy only applies to when the WEA alert is presented as there is intentional overshoot in order to cover 100% of the alert area, and a WEA-capable mobile device may receive a WEA broadcast outside the Alert Area but not present it to the mobile device user as part of DBGF, the accuracy is expected to be very high even with the Broadcast Area being greater than the Alert Area.
However, there are valid cases when DBGF-capable devices will present the WEA while the mobile device is outside the Alert Area. While there are a few reasons for this, they all involve the device not knowing or calculating its location, so as such would have no distance to report.
The primary cases for Overshoot are when the mobile device is within the
Broadcast Area but:
  is unable to determine its location,
  the user has location turned off, or
  the alert originator specifies DBGF Bypass due to the time sensitive nature of the WEA.
Performance Data options for accuracy from the Mobile Device:
  An indication that the WEA was presented inside or outside the Alert Area

## Slide 66: Automated Reporting from Staged Devices
This proposal describes a variation of automated reporting from mobile devices which would specifically employ staged devices. Similar to the proposal of reporting from opted-in consumer devices, this proposal would involve the design of a new device capability that would trigger reporting of various data from the staged devices, as well as the need to establish a data collection entity. The staged devices would be stationary with a known location, access to power, and a data connection.

## Slide 67: Automated Reporting from Staged Devices
Reliability
Reported by Alert Originators:
  Alert Area definition (geocode, and geometric coordinates if applicable)
  Languages provided (English 90, English 360, Spanish 90, Spanish 360)
Reported by all Stakeholders: (pertains to all metrics)
  Correlation data (Specifics TBD)
Latency
Reported by Device:
  Time of reception
  Time of presentation
Reported by FEMA:
  Time the alert was received
  Time the alert was sent to the CMSPs
Reported by the CMSP
  Time the alert was received
  Time the alert was first broadcast
  NOTE: Rather than having FEMA and the CMSPs report each time, a series of State/Local WEA Tests could be performed to determine an expected average. This timing does not vary significantly.
Accuracy
Known device data as well as reported data listed above for Reliability would meet requirements. No additional data needed.

## Slide 68: Recommendations
CSRIC VIII recommends that the FCC consider all findings in this report.
CSRIC VIII recommends that the FCC consider a requirement for an automated email to convey WEA performance reporting information from CMSPs and from PBS to an AO, or a centralized reporting location, for each sent WEA. Details for the generation procedures and content of the email automated performance report are encouraged to be worked out between AOs and CMSPs/PBS in a new ATIS WEA standard to support WEA automated performance reporting via email.
Additional Perspectives:
  Alert Originator Perspectives on WEA Automated Performance Reporting (See Section 5.2.1 of the Report)
  Cellular Industry Perspectives (See Section 5.2.2 of the Report)

## Slide 69
AO | Alert Originator
CMSP | Commercial Mobile Service Provider
DBGF | Device-Based Geo-Fencing
EAS | Emergency Alert System
FCC | Federal Communications Commission
FEMA | Federal Emergency Management Agency
IMEI | International Mobile Equipment Identity
IMEISV | IMEI Software Version
IPAWS | Integrated Public Alert & Warning System
Lat/Long | Latitude/Longitude
PBS | Public Broadcast System
TAC | Type Allocation Code
WEA | Wireless Emergency Alert
Type Allocation Code (TAC) | TAC is the initial eight-digit portion of the 15-digit International Mobile Equipment Identifier (IMEI) and 16-digit IMEI Software Version (IMEISV) codes used to uniquely identify wireless devices. The TAC identifies a particular model (and often revision) of wireless device for use on a 3GPP wireless network.

## Slide 70
CSRIC VIII Work Group 6 Report on WEA Performance Reporting
Submitted for CSRIC VIII Council Consideration

## Slide 71: Discussion
WG6: Co-chairs
Farrokh Khatibi, Qualcomm Francisco Sanchez, SBA
Report on WEA Performance Reporting

## Slide 72: Call For Vote
WG6: Co-chairs
Farrokh Khatibi, Qualcomm Francisco Sanchez, SBA
Report on WEA Performance Reporting

## Slide 73: Presentation
WG1: Co-chairs
Brian Daly, AT&T
Travis Russell, Oracle
WG1: 5G Signaling Protocols Security

## Slide 74: Working Group 1: 5G Signaling Protocols Security
December 15, 2022
Co-chairs:
Brian Daly, AT&T
Travis Russell, Oracle Communications
FCC Liaison: Ahmed Lahjouji

## Slide 75: Working Group 1: Background
The Chairwoman of the FCC directs CSRIC VIII to examine and address security vulnerabilities associated with the newly adopted 5G signaling protocol, Hypertext Transfer Protocol Version 2 (HTTP/2), which, like the SS7 and Diameter signaling protocols considered in earlier CSRICs, is vulnerable to attacks. Researchers have discovered security issues related to the HTTP/2 protocol which could place millions of websites at risk of attack. CSRIC VIII will confirm these vulnerabilities and identify others, assess their potential for harm, and recommend safeguards to harden 5G networks and protect critical business and consumer data from these and other cyber threats. CSRIC VIII will also provide recommendations on how to remediate the risks associated with HTTP/2 and prevent them from carrying over to HTTP/3, the next release of the protocol.

## Slide 76: Working Group 1: Objectives
The FCC has learned of four main vulnerabilities and attack vectors related to HTTP/2:
  (1) slow read attacks, which call on a malicious client to read responses very slowly;
  (2) HPACK Bombs, which are malicious archive files designed to crash the program or system reading them and often disable antivirus software;
  (3) Dependency Cycle attacks, which exploit a new flow mechanism designed to optimize networks to instead create an infinite loop which cannot be escaped; and
  (4) Stream Multiplexing Abuse, which uses security flaws in stream multiplexing functionality to crash servers, resulting in a denial of service to legitimate users.
We will research these as well as other vulnerabilities and attack vectors identified by industry through industry SMEs and WG member expertise.

## Slide 77
Working Group 1: Members
  *Also a CSRIC VIII Member
  Colin B. Andrews,* Telecommunications Industry Association
  Michael Bergman,* Consumer Technology Association
  Matt Carothers, Cox Communications
  Martin Goldberg,* National Security Agency
  Angel V. Gomez, Verizon Communications
  Stephen Hayes,* Ericsson
  Jithin Jagannath, ANDRO Computational Solutions
  Antwane Johnson,* FEMA
  Xiaoyang Lee, CISA
  John Marinho, CTIA
  Martin McGrath, Nokia
  Maureen C. Mclaughlin,* Satellite Industry Association
  Danny McPherson,* Verisign, Inc.
  Derek Peterson,* Wireless Broadband Alliance
  Mitch Rappard, Palo Alto Networks
  Mike Recchione, ATIS
  Christopher Wendt, Somos, Inc.
Co-chairs: Brian Daly,* AT&T
Travis Russell,* Oracle
FCC Liaison: Ahmed Lahjouji

## Slide 78
Working Group 1: Alternates*
* Alternates are not a member of the Working Group and may not vote.
  Adam Barron, Verizon Communications
  Martin C. Dolly, AT&T, Inc.
  Carroll Gray-Preston, ATIS
  J. David Grossman, CTA
  Brandon Hinton, Satellite Industry Association
  Bradley Jackson, Verizon Communication
  Navin Jaffer, CISA
  Yong Kim, Verisign, Inc.
  Mark Lucero, FEMA
  John Mattson, Ericsson

## Slide 79: Working Group 1: Deliverables/Schedule
WG virtual meetings (biweekly) continue
  Research/examine security vulnerabilities and attack vectors
Report on Security Vulnerabilities in HTTP/2 was submitted during the September 2022 CSRIC meeting
Report on Best Practices to Mitigate Vulnerabilities in HTTP/2, June 2023

## Slide 80: Status of Work
We are actually well ahead of schedule and will have no trouble meeting the deadline for the second report.
We did elect to take a different approach and add to the first report with sections on mitigation and recommendations rather than create a brand-new report with cut and paste from the first report

## Slide 81: Discussion
WG1: Co-chairs
Brian Daly, AT&T,
Travis Russell, Oracle
WG1: 5G Signaling Protocols Security

## Slide 82: Presentation
WG4: Co-chairs
Mary Boyd, Intrado
Mark Reddish, APCO
WG4: 911 Service Over Wi-Fi

## Slide 83: Working Group 4: 911 Service Over Wi-Fi
December 15, 2022
Co-chairs:
Mary Boyd, Intrado Life & Safety
Mark Reddish, APCO
FCC Liaison: Rasoul Safavian

## Slide 84: Working Group 4: Background
The Chairwoman of the FCC directs CSRIC VIII to explore the public safety benefits, technical feasibility, and cost of options for making Wi-Fi access points and/or unlicensed spectrum available to the public to facilitate access to 911 services. The ubiquitous nature of Wi-Fi access points suggests that, in the long term, various Wi-Fi solutions could be added to the “toolbox” of 911 connectivity options available to consumers, Public Safety Answering Points (PSAPs), and communications providers, and could complement the broader transition to an IP-based Next Generation 911 environment.

## Slide 85: Working Group 4: Objectives
Bring industry stakeholders together to examine a range of technical issues with the goal of promoting consensus in the Wi-Fi ecosystem to support reliable 911 services (voice and text) under normal conditions and when catastrophic events disrupt mobile service. The primary focus will be to:
examine and report on security issues including authentication and access control protocols, solutions to automatically activate Wi-Fi Calling on eligible mobile devices, when necessary;
automatically determining the 911 caller location and call routing issues, 911 call prioritization, identifying missing standards, and timelines and costs for implementing 911 over Wi-Fi solutions.

## Slide 86
Working Group 4: Members
  *Also a CSRIC VIII Member
Brandon Abley,* National Emergency Number Association
Rob Alderfer,* Charter Communications
Mark Annas,* City of Riverside Fire Department, OEM
Michael Bergman,* Consumer Technology Association
Wade Buckner,* International Association of Fire Chiefs
Kirk Burroughs, Apple
Chinmay Dhodapkar, Google LLC
Stephen Edge, Qualcomm Technologies, Inc.
Katherine Elkins,* NHTSA
Harold Feld,* Public Knowledge
Fred Frantz, ANDRO Computational Solutions
Mark Gibson, CommScope
James D. Goerke, Texas 9-1-1 Alliance
Jeanna M. Green, T-Mobile
Kevin Green, Somos, Inc.
Mark Grubb, CISA
Mark Hess,* Comcast Corporation
Craig Hodan,* National Weather Service/NOAA
Everett Kaneshige,* NATOA
Robert Kubik, Samsung Electronics America
William 'Andy' Leneweaver, Washington State Military Department
Jason Lish,* Lumen Technologies, Inc.
William Mikucki, Comtech Telecommunications
Susan Miller,* ATIS
Charles (“Peter”) Musgrove, AT&T, Inc.
Theresa Reese, Ericsson
Travis Reutter,* ACA Connects- America's Communications Association
Charlie Sasser, National Association of State Technology Directors
Tim Schram,* NARUC
Sean Scott,* SecuLore Solutions
Malcolm Smith, Cisco Systems, Inc.
Stuart Strickland, Hewlett Packard Enterprise
Jeff Torres, Verizon Communications
Steve Watkins,* Cox Communications
Jeffrey Wittek, Motorola Solutions
Co-chairs: Mary Boyd,* Intrado
Mark Reddish,* APCO
FCC Liaison: Rasoul Safavian

## Slide 87
Working Group 4: Alternates*
* Alternates are not a member of the Working Group and may not vote.
  Chris Anderson, Lumen Technologies, Inc.
  Carol Ansley, Cox Communications
  Scott Blue, Cisco
  Tom Breen, SecuLore Solutions
  Matthew Chappell, Cox Communications
  Justen Davis, Somos, Inc.
  Nicholas Garcia, Public Knowledge
  J. David Grossman, CTA
  Michael Hooker, T-Mobile
  Brian Hurley, ACA Connects
  Christian Militeau, ATIS
  Darrin Morkunas, Intrado
  James B. Ramsay, NARUC
  Praveen Srivastava, Charter Communications
  Megan Stapleton, Comtech Telecommunications
  Brian Tegtmeyer, NHTSA
  Peter Thornycroft, Hewlett Packard Enterprise
  Alison Venable, APCO

## Slide 88: Working Group 4: Deliverables/Schedule
Sub-Teams established:
  Technical Feasibility (Active)
  Public Safety Benefits (Active)
  Cost Analysis
Meeting Schedules:
  Bi-Weekly (Full WG)
  Weekly / Bi-Weekly (Sub-Teams)
Baseline Report – In draft
Final Report on 911 Service over Wi-Fi, March 2023

## Slide 89: Working Group 4: Samples of Anticipated Report
Completed
  Framework for report contributions
  Framework for use case analysis
  Background information on 911 over Wi-Fi and public safety benefits
  Analysis of current network architectures / emergency call flow
  Outline of current and potential 911 over Wi-Fi use cases
  Use case analysis (partial)
In progress
  Additional use case analyses
  Cost Analysis
  Recommendations

## Slide 90: Working Group 4: Next Steps
Weekly & bi-weekly meetings continue with extended length
Considering an in-person meeting
Continuing development of report contributions
Editing of draft report
On track for March 2023 completion

## Slide 91: Discussion
WG4: Co-chairs
Mary Boyd, Intrado
Mark Reddish, APCO
WG4: 911 Service Over Wi-Fi

## Slide 92: Presentation
WG5: Managing Software & Cloud Services Supply Chain Security for Comm. Infrastructure
WG5: Co-Chairs
Todd Gibson, T-Mobile
Padma Sudarsan, VMware

## Slide 93: Working Group 5: Managing Software & Cloud Services Supply Chain Security for Communications Infrastructure
December 15, 2022
Co-Chairs: Todd Gibson, T-Mobile & Padma Sudarsan, VMWare
FCC Liaison: Saswat Misra

## Slide 94: Working Group 5: Background
The Chairwoman of the FCC directs CSRIC VIII to review risks to service provider operations from attacks in service providers’ software and cloud services stacks and develop mitigation strategies for these vulnerabilities. In order to improve supply chain security in the communications industry, the FCC has barred the use of Universal Service Fund support to pay for equipment and services produced or provided by any company posing a national security threat to the integrity of communications networks or the communications supply chain, and the FCC will be reimbursing providers to remove, replace, and dispose of insecure equipment and services. Additionally, prior CSRIC work, such as the CSRIC IV Report on Cybersecurity Risk Management and Best Practices (March 2015), and the CSRIC II Report on Cybersecurity Best Practices (March 2011), focused on attacks that mostly affect traffic on the network or attacks on users through the network.
However, recent breaches of trusted vendors of software have exposed risks in other segments of the supply chain that have resulted in previously trusted systems becoming compromised. Specifically, attackers have inserted malware in to signed code with valid, but compromised, digital certificates. These recent breaches have highlighted that the threat is pervasive and extends well beyond the telecommunications network itself to software components and cloud-based services that service providers rely on to manage and operate their networks. Attacks on these operational networks could have a significant impact on emergency 911 calls and national security communications.
The FCC further directs CSRIC VIII to recommend best practices to mitigate the risks for each vulnerability it identifies, considering the matrix of capabilities of large and small service providers, large and small software vendors, and large and small cloud service providers.

## Slide 95
  *Also a CSRIC VIII Member
Rob Alderfer,* Charter Communications
Tom Anderson, ATIS
Colin Andrews, Telecommunications Industry Association
Jan H.L. (John-Luc) Bakker, BlackBerry Corporation
Donna Bethea-Murphy,* Inmarsat
Shirley Bloomfield,* NTCA-The Rural Broadband Association
Matt Carothers, Cox Communications
Josh Cech, S&T Telephone Cooperative Association
Ben Goldsmith,* Department of Justice
Dana Golub,* Public Broadcasting Service
Anu Jagannath, ANDRO Computational Solutions
Mohammad Khaled, Ericsson
Jason Lish,* Lumen Technologies, Inc.
Timothy May,* NTIA
Martin McGrath, Nokia
Maureen C. Mclaughlin,* Satellite Industry Association
Travis Reutter,* ACA Connects- America's Communications Association
Nasrin Rezai,* Verizon Communications
John Roznovsky, Mavenir
Sean Scott,* SecuLore Solutions
Jim Stringer, AT&T, Inc.
Richard “Dick” Tenney, CISA
Claire Vishik,* Intel
Kelly Williams, NAB
Timothy Wilson-Johnston, Cisco Systems, Inc.
Henry Young,* BSA | The Software Alliance
Co-Chairs: Todd Gibson, T-Mobile & Padma Sudarsan,* VMware
FCC Liaison: Saswat Misra
Working Group 5: Members

## Slide 96
* Alternates are not a member of the Working Group and may not vote.
  Reza Arefi, Intel
  Tom Breen, SecuLore Solutions
  Mark Carmel, CISA
  Cathleen M. Dwyer, Verizon Communications
  Brandon Hinton, Satellite Industry Association
  Brian Hurley, ACA Connects
  Tamber Ray, NTCA - The Rural Broadband Association
  Mark Roy, Public Broadcasting Service
  John A. Schiel, Lumen Technologies, Inc.
  Mike Regan, Telecommunications Industry Association
  Jason VonBargen, Charter Communications
  Timothy Youngblood,** T-Mobile
Working Group 5: Alternates*
  ** Also, a CSRIC VIII Member

## Slide 97: Working Group 5: Milestones/Schedule
Completed Milestone:
Best Practices to Improve Communications Supply Chain Security, September 2022
Next Milestone:
Best Practices to Improve Supply Chain Security of Infrastructure and Network Management Systems, June 2023
  Focus will be on Hardware Supply Chain and Implicit Trust of NMS Software Supply Chain
Meeting Schedule:
  Currently once every two weeks

## Slide 98: Working Group 5: Progress
Completed SME Presentations
  Tom Anderson, ATIS –Infra. and Network Management Supply Chain Security
  Chris Oatway, Verizon – Co-Chair for the DHS ICT SCRM Task Group
  Carlos Manzanares, Nokia – Network Control and Management
Scheduled SME Presentations
  Ericsson, Hardware Security (12/16/2022)
  Rakuten (1/13/23)
  Cloud Provider (VMware 1/27/23) and others TBD
  Other Mobile Network Operator Perspective (Still Developing)

## Slide 99: Working Group 5: Progress
Infrastructure and Network Management Systems Definitions
  WG aligned our definitions with the FCC Chairwoman’s office
  WG may update the definitions as the SME presentations continue
Draft Report document Framework Completed
  Our 2 co-rapporteurs shared the framework with the WG in our Nov 18 meeting

## Slide 100: Working Group 5: Next Steps
Report Section Assignments
  Start assigning names to author specific subsections.
SME Presentations
  Continue with those already scheduled
  Firm up the dates for those that are still unscheduled or TBD

## Slide 101: Discussion
WG5: Managing Software & Cloud Services Supply Chain Security for Comm. Infrastructure
WG5: Co-Chairs
Todd Gibson, T-Mobile
Padma Sudarsan, VMware

## Slide 102: Closing Remarks
CSRIC VIII Co-chair
Billy Bob Brown, CISA

## Slide 103: Adjourn Meeting Suzon Cameron, DFO

## Slide 104: NEXT CSRIC VIII MEETING March 21, 2023 at 1:00 pm EST